## Slide 1
UNIT 1
Chapter 1.1
Introduction to Microcontrollers

## Slide 2
Types of Microcontrollers
Microcontrollers are divided into various categories based on memory, architecture, bits and
instruction sets. Following is the list of their types −
Bit
Based on bit configuration, the microcontroller is further divided into three categories.
8-bit microcontroller − This type of microcontroller is used to execute arithmetic and
logical operations like addition, subtraction, multiplication division, etc. For example, Intel 8031 and 8051 are 8 bits microcontroller.
16-bit microcontroller − This type of microcontroller is used to perform arithmetic and
logical operations where higher accuracy and performance is required. For example, Intel 8096 is a 16-bit microcontroller.
32-bit microcontroller − This type of microcontroller is generally used in automatically controlled appliances like automatic operational machines, medical appliances, etc.

## Slide 3
Types of Microcontrollers
Memory
Based on the memory configuration, the microcontroller is further divided into two categories.
External memory microcontroller − This type of microcontroller is designed in such a way that they do not have a program memory on the chip. Hence, it is named as external memory microcontroller. For example: Intel 8031 microcontroller.
Embedded memory microcontroller − This type of microcontroller is designed in such a
way that the microcontroller has all programs and data memory, counters and timers, interrupts, I/O ports are embedded on the chip. For example: Intel 8051 microcontroller.

## Slide 4
Types of Microcontrollers
Instruction Set
Based on the instruction set configuration, the microcontroller is further divided into two
categories.
CISC − CISC stands for Complex Instruction Set Computer. It allows the user to insert a
single instruction as an alternative to many simple instructions.
RISC − RISC stands for Reduced Instruction Set Computer. It reduces the operational time by shortening the clock cycle per instruction.

## Slide 5
Comparison between 8-bit, 16-bit and 32-bit Microcontroller
The 8-bit, 16-bit and 32-bit microcontrollers are not very different in terms of cost but they can be deferred based upon their power usage, execution time, peripheral counts, I/O counts, etc. The 8-bit microcontroller processes with 8-bits of the data bus, which means this microcontroller can move 8-bits of data in a particular time frame. Then there is a 16-bit microcontroller and as the name implies, theoretically, it is two times faster than an 8-bits controller, and finally, there are the 32-bit microcontrollers. The 32-bits microcontrollers can move more data in a particular time frame as compared to 8-bit and 16-bit, as 32K is larger than both 8 and 16. For that reason, a 32- bit microcontroller can handle the quadruple amount of data as compared to the 8-bit and 16- bit processors which make the 32-bit microcontroller more data-efficient. But it makes the processor more power-hungry.

## Slide 6
Comparison between 8-bit, 16-bit and 32-bit Microcontroller
Arithmetic Operation: As per arithmetic operations, these microcontrollers are different
from each other. Each type of microcontroller has its own range of data set. For an 8-bit microcontroller, it can handle only 0 to 255 bits and 16-bit can handle 0 to 65,535 and a 32-bit microcontroller can handle up to 0 to 4,29,49,67,295. When data width becomes large, the microcontroller’s arithmetic core allows the controller to compute a large amount of data in an instant.
Memory: Like clock speed, a 32-bit microcontroller also comes at the top of the list.
Because in general, the memory capacity of a 32-bit microcontroller has eight times more memory than the 8-bit and 4 times more than a 16-bit microcontroller.

## Slide 7
Comparison between 8-bit, 16-bit and 32-bit Microcontroller
Clock Speed: When we talk about the difference between microcontrollers, the data
processing speed is a big factor to consider. In a microcontroller, data is processed in a particular time frame and the time it takes to process this data is dependent upon the Crystal Oscillator and depending upon the microcontroller type it can be an internal or external clock. 1Mhz crystal is equal to 1000000 cycles/second. So, 1 cycle is an execution of 1 instruction or data processing. The 8-bit and 16-bit microcontrollers are supported up to 40-64Mhz of the crystal, where a 32-bit microcontroller can support
>100Mhz crystal. Which makes the 32-bit microcontroller a more time-efficient
microcontroller. But there is also a drawback, that is more clock speed is equal to more power consumption.

## Slide 8
Comparison between 8-bit, 16-bit and 32-bit Microcontroller
Form Factor: According to the hardware’s structural form of a microcontroller, it is not true that the 32-bit microcontroller always comes in a larger package form (like TQFP, QFP, VTLA, TFBGA). Some 8-bit or 16-bit microcontrollers also come into the same form with the same number of pins (In that case some pins are not connected to the microcontroller).
Peripherals: If we compare the 8-bit and 16-bit microcontrollers to a 32-bit
microcontroller, we can clearly observe the difference. In a certain scenario if there is a need of Ethernet, CAN, USB, Modbus, and more, we have to choose a 32-bit microcontroller, because it comes bundled with these features, and in general, they also have necessary software support because 8-bit or 16-bit microcontrollers are insufficient for that reason we need to add peripheral ICs to resolve those issues but its effect on the cost.

## Slide 9
Advantages & Disadvantages of Microcontrollers
Advantages | Disadvantages
Design is more compact and easy to use. | They have a complex architecture.
The cost of a microcontroller is very cheap. | They are not suitable for high-power devices.
All the pins which are present in the microcontroller can be programmed. | They can perform only limited operations at the same time.
The interfacing of the ROM, RAM, and also the I/O ports is very simple and easy. | It is generally used only in any micro equipment.
Troubleshooting is quick, easy, and convenient. | It has limitations on the capacity of the storage of data.
Data is stored well, and even on reset, it won’t be erased. | It can overheat very quickly since it is tiny and has a complex set of peripherals

## Slide 10
Applications of Microcontrollers
Microcontrollers are widely used in various different devices such as −
Light sensing and controlling devices like LED.
Temperature sensing and controlling devices like microwave oven, chimneys.
Fire detection and safety devices like Fire alarm.
Measuring devices like Volt Meter.