## Slide 1
8051 Instructions
Instruction Syntax
General syntax for 8051 assembly language is as follows.
LABEL: OPCODE OPERAND
; COMMENT
LABEL: (THIS IS NOT NECESSARY UNLESS THAT SPECIFIC LINE HAS TO BE
ADDRESSED). The label is a symbolic address for the instruction. When the program is assembled, the label will be given specific address in which that instruction is stored. Unless that specific line of instruction is needed by a branching instruction in the program, it is not necessary to label that line.
OPCODE: Opcode is the symbolic representation of the operation. The assembler converts the opcode to a unique binary code (machine language).

## Slide 2
OPERAND: While opcode specifies what operation to perform, operand specifies where to
perform that action. The operand field generally contains the source and destination of the data. In some cases, only source or destination will be available instead of both. The operand will be either address of the data, or data itself.
COMMENT: Always comment will begin with ; or // symbol. To improve the program quality, programmer may always use comments in the program.

## Slide 3
ADDRESSING MODES
Various methods of accessing the data are called addressing modes. 8051 addressing modes are classified as follows.
Immediate addressing
Register addressing
Direct addressing
Indirect addressing
Indexed addressing
Bit addressing
Absolute addressing

## Slide 4
1. Immediate addressing. In this addressing mode the data is provided as a part of instruction itself. In other words, data immediately follows the instruction.
E.g. MOV A, #30H
ADD A, #83 ; # Symbol indicates the data is immediate.
2. Register addressing. In this addressing mode the register will hold the data. One of the eight general registers (R0 to R7) can be used and specified as the operand.
E.g. MOV A, R0
ADD A, R6
R0 – R7 will be selected from the current selection of register bank. The default register bank will be bank 0.
4. Indirect addressing. The indirect addressing mode uses a register to hold the actual address that will be used in data movement. Registers R0 and R1 and DPTR are the only registers that can be used as data pointers. Indirect addressing cannot be used to refer to SFR registers. Both R0 and R1 can hold 8-bit address and DPTR can hold 16-bit address.
E.g.
MOV A, @R0 ADD A, @R1 MOVX A, @DPTR

## Slide 5
3. Direct addressing. There are two ways to access the internal memory. Using direct address and indirect address. Using direct addressing mode, we can not only address the internal memory but SFRs also. In direct addressing, an 8-bit internal data memory address is specified as part of the instruction and hence, it can specify the address only in the range of 00H to FFH. In this addressing mode, data is obtained directly from the memory.
E.g. MOV A, 60h
ADD A, 30h
4. Indirect addressing. The indirect addressing mode uses a register to hold the actual address that will be used in data movement. Registers R0 and R1 and DPTR are the only registers that can be used as data pointers. Indirect addressing cannot be used to refer to SFR registers. Both R0 and R1 can hold 8-bit address and DPTR can hold 16-bit address.
E.g. MOV A, @R0
ADD A, @R1
MOVX A, @DPTR

## Slide 6
  5. Indexed addressing. In indexed addressing, either the program counter (PC), or the data pointer (DTPR)—is used to hold the base address, and the A is used to hold the offset address. Adding the value of the base address to the value of the offset address forms the effective address. Indexed addressing is used with JMP or MOVC instructions. Look up tables are easily implemented with the help of index addressing.
  E.g. MOVC A, @A+DPTR //copies the contents of memory location pointed by the sum of the accumulator A and the DPTR into accumulator A.
  MOVC A, @A+PC // copies the contents of memory location pointed by the
  sum of the accumulator A and the program counter into accumulator A.

## Slide 7
6. Bit Addressing Mode. Bit addressing mode is specifically designed to manipulate individual bits within the Special Function Registers (SFRs) of the 8051 microcontroller. SFRs are a set of memory-mapped hardware registers used for controlling various on-chip peripherals. This mode allows reading or modifying specific bits within these registers.
E.g. SETB P1.2 ; sets bit 2 of Port 1
7. Absolute addressing. Absolute addressing is used only by the AJMP (Absolute Jump) and ACALL (Absolute Call) instructions. These are 2 bytes instructions. The absolute addressing mode specifies the lowest 11 bit of the memory address as part of the instruction. The upper 5 bit of the destination address are the upper 5 bit of the current program counter. Hence, absolute addressing allows branching only within the current 2 Kbyte page of the program memory.
E.g.
AJMP LOOP1 ACALL LOOP2
A. TEXTBOOKS/REFERENCE BOOKS

## Slide 8
A. TEXTBOOKS/REFERENCE BOOKS
TEXTBOOKS
T1 Kenneth Ayala, The 8051 Microcontroller, Cengage Learning India, 3rd Edition, Nov 2007
T2 B. Kanta Rao, Embedded Systems, PHI, 1st Edition, January 2011
T3 John Boxall, Arduino Workshop: A Hands-On Introduction with 65 Projects, No Starch Press, 1st Edition, May 2013
REFERENCE BOOKS
R1 B. Ram, Fundamentals of Microprocessors and Microcontrollers, DRP, 8th Edition, Nov 2021
R2 Massimo Banzi, Getting Started with Arduino, Make Community LLC, 3rd Edition, Jan 2015
R3 Jeremy Blum, Exploring Arduino: Tools and Techniques for Engineering Wizardry, Wiley, 1st Edition, Aug 2013
B. Video Links:
https://www.youtube.com/watch?v=wQTXqCohOMM
https://www.youtube.com/watch?v=P1NlfPa-Idw