## Slide 1
Assembly Language
Assembler Directives
Assembler directives tell the assembler to do something other than creating the machine code for an instruction. In assembly language programming, the assembler directives instruct the assembler to-
Process subsequent assembly language instructions
Define program constants
Reserve space for variables

## Slide 2
The following are the widely used 8051 assembler directives.
ORG (origin). The ORG directive is used to indicate the starting address. It can be used only when the program counter needs to be changed. The number that comes after ORG can be either in hex or in decimal.
E.g. ORG 0000H ; Set PC to 0000.
EQU and SET. EQU and SET directives assign numerical value or register name to the specified symbol name. EQU is used to define a constant without storing information in the memory. The symbol defined with EQU should not be redefined. SET directive allows redefinition of symbols at a later stage.
DB (DEFINE BYTE). The DB directive is used to define an 8 bit data. DB directive initializes memory with 8-bit values. The numbers can be in decimal, binary, hex or in ASCII formats. For decimal, the 'D' after the decimal number is optional, but for binary and hexadecimal, 'B' and ‘H’ are required. For ASCII, the number is written in quotation marks (‘LIKE This).

## Slide 3
DATA1: DB 40H ; hex
DATA2: DB 01011100B ; binary
DATA3: DB 48 ; decimal
DATA4: DB 'HELLO W’ ; ASCII
END. The END directive signals the end of the assembly module. It indicates the end of the program to the assembler. Any text in the assembly file that appears after the END directive is ignored. If the END statement is missing, the assembler will generate an error message.

## Slide 4
INSTRUCTION SET
Instruction Timings. The 8051 internal operations and external read/write operations are controlled by the oscillator clock. T-state, Machine cycle and Instruction cycle are terms used in instruction timings.
state is defined as one subdivision of the operation performed in one clock period. The terms 'T- state' and 'clock period' are often used synonymously.
Machine cycle is defined as 12 oscillator periods. A machine cycle consists of six states and each
state lasts for two oscillator periods. An instruction takes one to four machine cycles to execute an instruction.
Instruction cycle is defined as the time required for completing the execution of an instruction. The 8051 instruction cycle consists of one to four machine cycles.

## Slide 5
Eg. If 8051 microcontroller is operated with 12 MHz oscillator, find the execution time for the following four instructions.
  ADD A, 45H
  SUBB A, #55H
  MOV DPTR, #2000H
  MUL AB
Since the oscillator frequency is 12 MHz, the clock period is, Clock period = 1/12 MHz = 0.08333
µS. Time for 1 machine cycle = 0.08333 µS x 12 =1 µ S.
Instruction No. of machine cycles Execution time
ADD A, 45H 1 1 µs
SUBB A, #55H 2 2 µs
MOV DPTR, #2000H 2 2 µs
MUL AB 4 4 µs

## Slide 6
8051 Instructions
The instructions of 8051 can be broadly classified under the following headings.
Data transfer instructions
Arithmetic instructions
Logical instructions
Branch instructions
Subroutine instructions
Bit manipulation instructions

## Slide 7
Data transfer instructions
In this group, the instructions perform data transfer operations of the following types.
  Move the contents of a register Rn to A
    MOV A,R2
    MOV A,R7
  Move the contents of a register A to Rn
    MOV R4,A
    MOV R1,A
  Move an immediate 8 bit data to register A or to Rn or to a memory location (direct or indirect)
        MOV A, #45H
        MOV R6, #51H
        MOV 30H, #44H
        MOV @R0, #0E8H
        MOV DPTR, #0F5A2H
        MOV DPTR, #5467H

## Slide 8
d. Move the contents of a memory location to A or A to a memory location using direct and indirect addressing
    MOV A, 65H
    MOV A, @R0
    MOV 45H, A
    MOV @R1, A
Move the contents of a memory location to Rn or Rn to a memory location using direct addressing
  MOV R3, 65H
  MOV 45H, R2
Move the contents of memory location to another memory location using direct and indirect addressing
  MOV 47H, 65H
  MOV 45H, @R0

## Slide 9
Move the contents of program memory to A
  MOVC A, @A+PC
  MOVC A, @A+DPTR
Move the contents of an external memory to A or A to an external memory
    MOVX A,@R1
    MOVX @R0,A
    MOVX A, @DPTR
    MOVX @DPTR, A

## Slide 10
FIG. Addressing Using MOV, MOVX and MOVC

## Slide 11
i. Push and Pop instructions
 | [SP]=07 | //CONTENT OF SP IS 07 (DEFAULT VALUE)
MOV R6, #25H MOV R1, #12H | [R6]=25H [R1]=12H | //CONTENT OF R6 IS 25H //CONTENT OF R1 IS 12H
MOV R4, #0F3H | [R4]=F3H | //CONTENT OF R4 IS F3H
PUSH 6 | [SP]=08 | [08]=[06]=25H | //CONTENT OF 08 IS 25H
PUSH 1 PUSH 4 | [SP]=09 [SP]=0A | [09]=[01]=12H [0A]=[04]=F3H | //CONTENT OF 09 IS 12H //CONTENT OF 0A IS F3H
POP 6 | [06]=[0A]=F3H | [SP]=09 | //CONTENT OF 06 IS F3H
POP 1 POP 4 | [01]=[09]=12H [04]=[08]=25H | [SP]=08 [SP]=07 | //CONTENT OF 01 IS 12H //CONTENT OF 04 IS 25H

## Slide 12
Exchange instructions. The content of source ie., register, direct memory or indirect memory will be exchanged with the contents of destination ie., accumulator.
  XCH A,R3
  XCH A,@R1
  XCH A,54h
Exchange digit. Exchange the lower order nibble of Accumulator (A0-A3) with
lower order nibble of the internal RAM location which is indirectly addressed by the register.
  XCHD A,@R1
  XCHD A,@R0

## Slide 13
2. Arithmetic instructions. The 8051 can perform addition, subtraction. Multiplication and division operations on 8 bit numbers.
Addition
In this group, we have instructions to
Add the contents of A with immediate data with or without carry.
  ADD A, #45H
  ADDC A, #0B4H
Add the contents of A with register Rn with or without carry.
  ADD A, R5
  ADDC A, R2
Add the contents of A with contents of memory with or without carry using direct and indirect addressing
  ADD A, 51H iii. ADD A, @R1
  ADDC A, 75H iv. ADDC A, @R0
CY AC and OV flags will be affected by this operation.

## Slide 14
Subtraction
In this group, we have instructions to
Subtract the contents of A with immediate data with or without carry.
  SUBB A, #45H
  SUBB A, #OB4H
Subtract the contents of A with register Rn with or without carry.
  SUBB A, R5
  SUBB A, R2
Subtract the contents of A with contents of memory with or without carry using direct and indirect addressing
  SUBB A, 51H
  SUBB A, 75H
  SUBB A, @R1
  SUBB A, @R0
CY AC and OV flags will be affected by this operation.

## Slide 15
Multiplication
MUL AB. This instruction multiplies two 8 bit unsigned numbers which are stored in A and B register. After multiplication the lower byte of the result will be stored in accumulator and higher byte of result will be stored in B register.
E.g. MOV A, #45H ;[A]=45H
MOV B, #0F5H ;[B]=F5H
MUL AB ;[A] X [B] = 45 X F5 = 4209
;[A]=09H, [B]=42H
Division
DIV AB. This instruction divides the 8 bit unsigned number which is stored in A by the 8 bit unsigned number which is stored in B register. After division the result will be stored in accumulator and remainder will be stored in B register.
E.g. MOV A, #45H ;[A]=0E8H
MOV B, #0F5H ;[B]=1BH
DIV AB ;[A] / [B] = E8 /1B = 08 H with remainder 10H
;[A] = 08H, [B]=10H

## Slide 16
DA A (Decimal Adjust After Addition). When two BCD numbers are added, the answer is a non-BCD number. To get the result in BCD, we use DA A instruction after the addition. DA A works as follows.
If lower nibble is greater than 9 or auxiliary carry is 1, 6 is added to lower nibble.
If upper nibble is greater than 9 or carry is 1, 6 is added to upper nibble.
E.g. 1: MOV A, #23H
MOV R1, #55H
ADD A, R1 // [A]=78
DA A // [A]=78 no changes in the accumulator after da a
E.g. 2: MOV A, #53H
MOV R1, #58H
ADD A, R1 // [A]=Abh
DA A // [A]=11, C=1. ANSWER IS 111. Accumulator data is changed after DA A

## Slide 17
Increment: Increments the operand by one.
INC A INC Rn INC DIRECT INC @RiINC DPTR
INC increments the value of source by 1. If the initial value of register is FFh, incrementing the value will cause it to reset to 0. The Carry Flag is not set when the value "rolls over" from 255 to 0.
In the case of "INC DPTR", the value two-byte unsigned integer value of DPTR is incremented. If the initial value of DPTR is FFFFh, incrementing the value will cause it to reset to 0.
Decrement: Decrements the operand by one.
DEC A DEC Rn DEC DIRECT DEC @Ri
DEC decrements the value of source by 1. If the initial value is 0, decrementing the value will cause it to reset to FFh. The Carry Flag is not set when the value "rolls over" from 0 to FFh.

## Slide 18
3. Logical Instructions
Logical AND
ANL destination, source. ANL does a bitwise "AND" operation between source and destination, leaving the resulting value in destination. The value in source is not affected. "AND" instruction logically AND the bits of source and destination.
ANL A, #DATA ANL A, Rn
ANL A, DIRECT ANL A, @Ri
ANL DIRECT, A ANL DIRECT, #DATA

## Slide 19
Logical OR
ORL destination, source. ORL does a bitwise "OR" operation between source and destination, leaving the resulting value in destination. The value in source is not affected. "OR" instruction logically OR the bits of source and destination.
ORL A, #DATA ORL A, Rn
ORL A, DIRECT ORL A, @Ri
ORL DIRECT, A ORL DIRECT, #DATA
Logical Ex-OR
XRL destination, source. XRL does a bitwise "EX-OR" operation between source and destination, leaving the resulting value in destination. The value in source is not affected. "XRL" instruction logically EX-OR the bits of source and destination.
XRL A, #DATA XRL A, Rn
XRL A, DIRECT XRL A, @Ri
XRL DIRECT, A XRL DIRECT, #DATA

## Slide 20
Logical NOT
CPL complements operand, leaving the result in operand. If operand is a single bit, then the state of the bit will be reversed. If operand is the accumulator, then all the bits in the Accumulator will be reversed.
CPL A CPL C CPL bit address
SWAP A – Swap the upper nibble and lower nibble of A.
This instruction is rotate right the accumulator. Its operation is illustrated below. Each bit is shifted one location to the right, with bit 0 going to bit 7.

## Slide 21
Rotate Instructions
RR A. This instruction is rotate right the accumulator. Its operation is illustrated below. Each bit is shifted one location to the right, with bit 0 going to bit 7.
RL A. Rotate left the accumulator. Each bit is shifted one location to the left, with bit 7 going to bit 0.

## Slide 22
Rotate Instructions
RRC A. Rotate right through the carry. Each bit is shifted one location to the right, with bit 0 going into the carry bit in the PSW, while the carry was at goes into bit 7.
RLC A. Rotate left through the carry. Each bit is shifted one location to the left, with bit 7 going into the carry bit in the PSW, while the carry goes into bit 0.

## Slide 23
4. Branch (JUMP) Instructions and Loops
Looping in the 8051
Repeating a sequence of instructions a certain number of times is called a loop. An instruction DJNZ reg, label is used to perform a Loop operation. In this instruction, a register is decremented by 1; if it is not zero, then 8051 jumps to the target address referred to by the label. The register is loaded with the counter for the number of repetitions prior to the start of the loop. In this instruction, both the registers decrement and the decision to jump are combined into a single instruction. The registers can be any of R0–R7. The counter can also be a RAM location.

## Slide 24
Example: Multiply 25 by 10 using the technique of repeated addition.
Solution − Multiplication can be achieved by adding the multiplicand repeatedly, as many times as the multiplier. For example,
25 * 10 = 250(FAH)
25 + 25 + 25 + 25 + 25 + 25 + 25 + 25 + 25 + 25 = 250
MOV A,#0 ; A = 0, clean ACC
MOV R2,#10 ; the multiplier is replaced in R2
Add A,#25 ; add the multiplicand to the ACC
AGAIN: DJNZ R2,
AGAIN: repeat until R2 = 0 (10 times)
MOV R5 , A ;save A in R5
;R5 (FAH)

## Slide 25
Drawback in 8051 − Looping action with the instruction DJNZ Reg label is limited to 256 iterations only. If a conditional jump is not taken, then the instruction following the jump is executed.
Looping inside a Loop
When we use a loop inside another loop, it is called a nested loop. Two registers are used to hold the count when the maximum count is limited to 256. So we use this method to repeat the action more times than 256.
Example
Write a program to −
Load the accumulator with the value 55H.
Complement the ACC 700 times.

## Slide 26
Solution − Since 700 is greater than 255 (the maximum capacity of any register), two registers are used to hold the count. The following code shows how to use two registers, R2 and R3, for the count.
MOV A,#55H ;A = 55H
NEXT: MOV R3,#10 ;R3 the outer loop counter
AGAIN:MOV R2,#70 ;R2 the inner loop counter
CPL A ;complement

## Slide 27
Jump and Call Program Range
There are 3 types of jump instructions. They are :
Relative Jump
Short Absolute Jump
Long Absolute Jump
Relative Jump. Jump that replaces the PC (program counter) content with a new address that is greater than (the address following the jump instruction by 127 or less) or less than (the address following the jump by 128 or less) is called a relative jump. Schematically, the relative jump can be shown as follows:

## Slide 28
The advantages of the relative jump are as follows:
Only 1 byte of jump address needs to be specified in the 2's complement form, ie. For jumping ahead, the range is 0 to 127 and for jumping back, the range is -1 to -128.
Specifying only one byte reduces the size of the instruction and speeds up program execution.
The program with relative jumps can be relocated without reassembling to generate absolute jump addresses.
Disadvantages of the relative jump:
1. Short jump range (-128 to 127 from the instruction following the jump instruction)

## Slide 29
Instructions that use Relative Jump
SJMP <relative address> ; this is unconditional jump
The remaining relative jumps are conditional jumps
JC <relative address>
JNC <relative address>
JB bit, <relative address>
JNB bit, <relative address>
JBC bit, <relative address>
CJNE <destination byte>, <source byte>, <relative address>
DJNZ <byte>, <relative address>
JZ <relative address>
JNZ <relative address>

## Slide 30
Short Absolute Jump. In this case only 11bits of the absolute jump address are needed. The absolute jump address is calculated in the following manner.
In 8051, 64 kbyte of program memory space is divided into 32 pages of 2 kbyte each. The hexadecimal addresses of the pages are given as follows:
Page (Hex) Address (Hex)
00 0000 - 07FF
01 0800 - 0FFF
02 1000 - 17FF
03 1800 - 1FFF
.
.
1E F000 - F7FF
1F F800 - FFFF

## Slide 31
It can be seen that the upper 5 bits of the program counter (PC) hold the page number and the lower 11bits of the PC hold the address within that page. Thus, an absolute address is formed by taking page numbers of the instruction (from the program counter) following the jump and attaching the specified 11bits to it to form the 16-bit address.
Advantage: The instruction length becomes 2 bytes. Example of short absolute jump: -
ACALL <address 11>
AJMP <address 11>
Long Absolute Jump/Call. Applications that need to access the entire program memory from 0000H to FFFFH use long absolute jump. Since the absolute address has to be specified in the op-code, the instruction length is 3 bytes (except for JMP @ A+DPTR). This jump is not re- locatable.
Example: -
LCALL <address 16>
LJMP <address 16> JMP @A+DPTR

## Slide 32
Another classification of jump instructions is
Unconditional Jump
Conditional Jump
The unconditional jump is a jump in which control is transferred unconditionally to the target location.
  LJMP (long jump). This is a 3-byte instruction. First byte is the op-code and
second and third bytes represent the 16-bit target address which is any memory location from 0000 to FFFFH
e.g: LJMP 3000H
b. AJMP: this causes unconditional branch to the indicated address, by loading
the 11-bit address to 0 -10 bits of the program counter. The destination must be therefore within the same 2K blocks.

## Slide 33
c. SJMP (short jump). This is a 2-byte instruction. First byte is the op-code and second byte is the relative target address, 00 to FFH (forward +127 and backward-128 bytes from the current PC value). To calculate the target address of a short jump, the second byte is added to the PC value which is address of the instruction immediately below the jump.
2. Conditional Jump instructions.
  JBC ; Jump if bit ＝ 1 and clear bit
  JNB ; Jump if bit ＝ 0
  JB ; Jump if bit ＝ 1
  JNC ; Jump if CY ＝ 0
  JC ; Jump if CY ＝ 1
  CJNE reg, #data ; Jump if byte ≠ #data
  CJNE A, byte ; Jump if A ≠ byte
  DJNZ ; Decrement and Jump if A ≠ 0
  JNZ ; Jump if A ≠ 0
  JZ ; Jump if A ＝ 0
  All conditional jumps are short jumps.

## Slide 34
Bit level jump instructions:
Bit level JUMP instructions will check the conditions of the bit and if condition is true, it jumps to the address specified in the instruction. All the bit jumps are relative jumps.
JB bit, rel ; jump if the direct bit is set to the relative address specified.
JNB bit, rel ; jump if the direct bit is clear to the relative address specified.
JBC bit, rel ; jump if the direct bit is set to the relative address specified and then clear the bit.

## Slide 35
5. Subroutine CALL And RETURN Instructions
Subroutines are handled by CALL and RET instructions There are two types of CALL instructions.
LCALL address (16 bit). This is long call instruction which unconditionally calls the subroutine located at the indicated 16-bit address. This is a 3-byte instruction. The LCALL instruction works as follows.
During execution of LCALL, [PC] = [PC]+3; (if address where LCALL resides is say, 0x3254; during execution of this instruction [PC] = 3254h + 3h = 3257h
[SP]=[SP]+1; (if SP contains default value 07, then SP increments and [SP]=08
[[SP]] = [PC7-0]; (lower byte of PC content i.e., 57 will be stored in memory location 08.
[SP]=[SP]+1; (SP increments again and [SP]=09)
[[SP]] = [PC15-8]; (higher byte of PC content i.e., 32 will be stored in memory location 09.
With these the address (0x3254) which was in PC is stored in stack.
[PC]= address (16 bit); the new address of subroutine is loaded to PC. No flags are affected.

## Slide 36
ACALL address (11 bit). This is absolute call instruction which unconditionally calls the subroutine located at the indicated 11-bit address. This is a 2-byte instruction. The SCALL instruction works as follows.
  During execution of SCALL, [PC] = [PC]+2 ; (if address where LCALL
resides is say, 0x8549 ; during execution of this instruction [PC] = 8549h + 2h = 854Bh
  [SP]=[SP]+1 ; (if SP contains default value 07, then SP increments and [SP]=08
  [[SP]] = [PC7-0] ; (lower byte of PC content ie., 4B will be stored in memory location 08.
  [SP]=[SP]+1 ; (SP increments again and [SP]=09)
  [[SP]] = [PC15-8] ; (higher byte of PC content i.e., 85 will be stored in memory location 09.
With these the address (0x854B) which was in PC is stored in stack.
  f. [PC10-0]= address (11 bit); the new address of subroutine is loaded to PC. No flags are affected.

## Slide 37
RET instruction. RET instruction pops top two contents from the stack and load it to PC.
[PC15-8] = [[SP]] ; content of current top of the stack will be moved to higher byte of PC.
[SP]=[SP]-1 ; SP decrements
[PC7-0] = [[SP]] ; content of bottom of the stack will be moved to lower byte of PC.
[SP]=[SP]-1 ; SP decrements again
Bit manipulation instructions.
8051 has 128-bit addressable memory. Bit addressable SFRs and bit addressable PORT pins. It is possible to perform following bit wise operations for these bit addressable locations.
  LOGICAL AND
    ANL C, BIT (BIT ADDRESS) ; ‘logically AND’ carry and content of bit address, store result in carry
    ANL C, /BIT; ; ‘logically and’ carry and complement of content of bit address, store result in carry

## Slide 38
  2. LOGICAL OR
    ORL C, BIT(BIT ADDRESS) ; ‘logically or’ carry and content of bit address, store result in carry
    ORL C, /BIT; ; ‘logically or’ carry and complement of content of bit address,
store result in carry
  3. CLR bit
    CLR bit ; content of bit address specified will be cleared.
    CLR C ; content of carry will be cleared.
4. CPL bit
      CPL bit ; content of bit address specified will be complemented.
      CPL C ; content of carry will be complemented.

## Slide 39
TEXTBOOKS/REFERENCE BOOKS
  TEXTBOOKS
T1 Kenneth Ayala, The 8051 Microcontroller, Cengage Learning India, 3rd Edition, Nov 2007
T2 B. Kanta Rao, Embedded Systems, PHI, 1st Edition, January 2011
T3 John Boxall, Arduino Workshop: A Hands-On Introduction with 65 Projects, No Starch Press, 1st Edition, May 2013
  REFERENCE BOOKS
R1 B. Ram, Fundamentals of Microprocessors and Microcontrollers, DRP, 8th Edition, Nov 2021
R2 Massimo Banzi, Getting Started with Arduino, Make Community LLC, 3rd Edition, Jan 2015
R3 Jeremy Blum, Exploring Arduino: Tools and Techniques for Engineering Wizardry, Wiley, 1st Edition, Aug 2013
Video Links:
  https://www.youtube.com/watch?v=paAiW-zZSTs
  https://www.youtube.com/watch?v=pC56UDhullM
  https://www.youtube.com/watch?v=pzf_gTTpUhM
  https://www.youtube.com/watch?v=EI3MtI93zu4