## Slide 1
Arduino String
The string is a data type that stores text rather than the integer values. It is similar to other data types such as integer, float, etc., in Arduino. The string is an array of characters or a set of characters that consists of numbers, spaces, and special characters from the ASCII table.
The string can be declared in the following ways:
char StrA[10];
o char StringA[8] = {'w', 'e', 'l', 'c', 'o', 'm', 'e'};
We can also add an explicit null character
o char StringB[8] = {'w', 'e', 'l', 'c', 'o', 'm', 'e', '\0'};
We can also declare an array with extra space for a string constant StrA.
char StrA[10]; = "Hello";
char StrD[6]; = "Hello";
char StrD[]; = "Welcome";

## Slide 2
The data type is char. Each character is an element in string. For example, Arduino contains seven characters. So, we need to declare an array atleast of size 8 (1 extra to store the null character at the end of the string).
Consider the below example:
char myString[len] = "text";
The above declared string will be stored as:
When we create a string using the double quotes like the word "text" specified above, the compiler automatically creates an element out of each character. It further appends the null character to the end.
The null character has the value 0 in the ASCII table. It is defined using two characters (\ and \0). The backslash (\) represents the special character when used in conjunction with other characters. The backslash is also known as an escape character. The null character is added by the compiler to terminate the string.
Note: Strings are always declared inside the double quotes, while characters are declared inside single quotes.

## Slide 3
How Serial.print() and Serial.println() works with strings?
It is interesting to know how print() and println() function works with the strings.
Serial.print() with string. Let's understand with a coding example.
const int length = 20;
char myString[length] = "Hello Arduino";
// we can also specify as char myString[20] = "Hello Arduino";
void setup()
{
Serial.begin(9600);
}

## Slide 4
void loop() {
for( int i=0; i<length; i = i+1) {
if(myString[i]== '\0’) {
// it will stop printing when it sees a null character
break;
}
Serial.print(myString[i]);
}
Serial.println();
delay(500);
}
The code will print Hello Arduino multiple times, as shown here:

## Slide 5
Serial.println() with string. In the case of println() function, we need not require any for loop or condition to print. It is an easier way to print strings. The println() function will work the same as the above.
Consider the below example.
const int length = 15;
char myString[length] = "Hello Arduino";
void setup() {
Serial.begin(9600);
}
void loop() {
7. Serial.println(myString);
8. delay(500);
9. }
Output:
The output will be the same as for previous one.

## Slide 6
Array of Strings
We can specify the array of strings while working with large projects, such as LCD display, etc.
The array names are also considered as pointers. The data type marked with an asterisk is defined as pointers.
For example, char*. To define an array of arrays, we actually need pointers. Let's understand with an example.
char *StrAB[] = {"Welcome to string A to G in Arduino", "Here is string A", "Here is str ing B", "Here is string C", "Here is string D", "Here is string E", "Here is string F", "Here is string G" };
void setup() {
Serial.begin(9600);
}

## Slide 7
void loop() {
for (int i = 0; i < 8; i++) {
Serial.println(StrAB[i]);
delay(1000);
}
}
Output:

## Slide 8
Arduino String Object
An object is like a variable, which points to a memory location that holds some data. The functions associated with the object are called member functions. As a result, we can make the objects to perform some actions.
For example,
The begin(), print(), and println() are the functions that are declared using the serial object. The period after the Serial (print(), etc.) specifies that we are accessing some members within the serial object. The members can be either a function or a variable.
The parentheses after the print() and println() function determines the function being called in the serial. These functions cannot be declared alone in the global scope in the code. Thus, they are declared with the serial object as Serial.print() and Serial.println().

## Slide 9
String Object
The String object allows us to store and perform actions on an array of characters. The String object takes more memory than the regular String. The String object is always displayed with the uppercase 'S'. It produces an instance of the String class.
It can be constructed from different data types, which are listed below:
a constant integer using a specific base
a long integer using a particular base
an instance of a String object
a constant character enclosed within a single-quotes
A constant string of characters enclosed within the double-quotes.
float and double

## Slide 10
The specified number in a string has a default base of 10. For example, String myString = String(15);
It creates a string that consists of the ASCII representation of the number 15. To specify a number with base other than 10, the String can be created as:
String myString = String(15, HEX);
It will give us the String ''F''. It signifies the hexadecimal conversion of the decimal number 15. We can also represent a String in BIN. For example,
String myString = String(15, BIN);
It will give us the String ''1111''. It signifies the hexadecimal conversion of the decimal number 15.
The syntax is:
1. String(value)
2. String(value, base)
3. String(value, PlacesofaDecimal)

## Slide 11
where,
value: It signifies the value needed to format or represent a string.
The data types are byte, unsigned int, char, float, double, unsigned long, long, int, and string. base: It signifies the base, which is required to format the integer value. For example, HEX, BIN, etc. The base is optional to include.
PlacesofaDecimal: It specifies the desired decimal places, which is only needed if the value is double or float.

## Slide 12
Functions with String Object
We can use various functions with the String.
charAT()
It is used to access a specific character.
The syntax is:
thisString.charAT(n)
where,
thisString is the declared variable
n is also a variable
The data type allowed is unsigned int. The above syntax will return the nth character of the specified string.

## Slide 13
compareTo()
It is used to compare the two Strings. The specified Strings are compared using the ASCII values
of the characters. The syntax is:
thisString.compareTo(myString)
where thisString and myString are the declared variable
The above syntax will return a negative number if thisString comes before myString. It will return a positive number if thisString comes after myString.
endsWith()
It tests that if a String ends with the characters of other String or not.
The syntax is:
thisString.endsWith(myString)
where thisString and myString are the declared variable
It will return true if thisString ends with the characters of myString. Otherwise, it will return false.

## Slide 14
startsWith()
It tests that if a String starts with the characters of other String or not.
The syntax is:
thisString.startsWith(myString)
where thisString and myString are the declared variable
It will return true if thisString starts with the characters of myString. Otherwise, it will return false.
toLowerCase()
It gets a lowercase version of the specified String.
The syntax is:
thisString.toLowerCase()
where thisString is the declared variable

## Slide 15
toUpperCase()
It gets an uppercase version of the specified String.
The syntax is:
thisString.toUpperCase()
where thisString is the declared variable
equals()
It compares the equality of the Two Strings. The comparison is quite sensitive, where String
"Arduino" is not equal to the String "ARDUINO". The syntax is:
thisString.equals(myString)
where thisString and myString are the variables
It will return true if thisString equals to myString. Otherwise, it will return false.

## Slide 16
getBytes()
It copies the characters of the String to the supplied buffer.
The syntax is:
thisString.getBytes(buffer, length)
where,
thisString is the declared variable
buffer: The characters are copied into the buffer. The required data type is the byte.
length: It signifies the size of the buffer. The required data type is unsigned int.
lastIndexOf()
It locates a String or character within the other String.
The syntax is:
thisString.lastIndexOf(value)
thisString.lastIndexOf(value, from) where,
thisString is the declared variable
value: It includes the particular value to search for. The required data types are String and char.
from: It is defined as the index to work backward from

## Slide 17
substring()
It is declared to get the substring of a specific String.
The syntax is:
thisString.substring(from)
thisString.substring(from, to) where,
thisString is the declared variable
from: It is defined as the index, from where the substring will start
to: It is also the index to end the substring before. It is optional.
toInt()
It converts a valid String in Arduino to the integer type.
The syntax is:
thisString.toInt()
where thisString is the variable
The required data type is long. It returns zero if the conversation is invalid or a String does not start with an integer number.

## Slide 18
toFloat()
It converts a valid String in Arduino to the float.
For example, String "150" will be converted to "150.00" The syntax is:
thisString.toFloat()
where thisString is the variable
The required data type is float. It returns zero if the conversation is invalid or a String does not start with a digit.
trim()
It modifies the String by removing the extra whitespaces.
The syntax is:
thisString.trim()
where thisString is the variable

## Slide 19
Code Examples
Let's understand the String Object with two examples.
Example 1:
Let's use the charAt() function. Consider the below code:
1. void setup() {
Serial.begin(9600);
String thisString = "Welcome to Arduino";
Serial.println(thisString.charAt(8));
}
void loop() { }
Output: t
The t is the character at index 8, which is declared in the charAt() function.

## Slide 20
Example 2:
concat() - The concat() function is used to combine the Strings.
Consider the below code:
void setup() {
Serial.begin(9600);
String thisString = “Welcome to Arduino”;
thisString.concat("String Object");
Serial.println(thisString);
}
void loop() { }
Output:
Similarly, we can use other String object functions as well.