## Slide 1
Arduino Variables
The variables are defined as the place to store the data and values. It consists of a name, value, and type. The variables can belong to any data type such as int, float, char, etc.
Consider the below example:
int pin = 8;
Here, the int data type is used to create a variable named pin that stores the value 8. It also means that value 8 is initialized to the variable pin. We can modify the name of the variable according to our choice.

## Slide 2
For example,
The above example can also be written as:
int LEDpin = 8;
Here, the variable name is LEDpin.
We can refer the declared variable further in our program or code.
For example,
pinMode(LEDpin, OUTPUT);
Here, the value stored (8) in the declared variable (LEDpin) will be passed to the pinMode() function.
If we have not declared the variable, the value can also be directly passed to the function.
For example:
pinMode( 8, OUTPUT);

## Slide 3
Advantages of Variables
The advantages of the variables are listed below:
We can use a variable many times in a program.
The variables can represent integers, strings, characters, etc.
It increases the flexibility of the program.
We can easily modify the variables. For example, if we want to change the value of variable LEDpin from 8 to 13, we need to change the only point in the code.
We can specify any name for a variable. For example, greenpin, bluePIN, REDpin, etc.
How can we change the value of a variable in Arduino?
The value of a variable can be changed using the assignment operator (equal = sign). But we need to declare a variable before assigning the value. If we directly specify the value as:
1. pin = 7;
We will get an error that pin has not declared.

## Slide 4
We can easily change the variables by copying its value to another variable. For example,
1. void setup() 2. {
Serial.begin(9600);
int pinLED = 7;
Serial.println(pinLED); // value 7 will be printed
int pin1 = pinLED;
pinLED = 13;
Serial.println(pinLED); // value is now changed
// now, value 13 will be printed
10. }
11. void loop()
12. {
13. }

## Slide 5
Output:
We can notice in the output that the value of LEDpin is changed from 7 to 13. Similarly, we can change the values of variables.
Variables Scope
It means that in how many ways the variables can be declared.
The variables can be declared in two ways in Arduino, which are listed below:
Local variables
Global variables

## Slide 6
Local Variables. The local variables are declared within the function. The variables have scope only within the function. These variables can be used only by the statements that lie within that function.
For example,
1. void setup()
2. {
3. Serial.begin(9600);
4. }
5. void loop()
6. {
int x = 3;
int b = 4;
int sum = 0;
sum = x + b;
Serial.println(sum);
12. }

## Slide 7
Global Variables. The global variables can be accessed anywhere in the program. The global variable is declared outside the setup() and loop() function.
For example,
Consider the below code.
int LEDpin = 8;
void setup()
{
4. pinMode(LEDpin, OUTPUT);
5. }
6. void loop()
7. {
8. digitalWrite(LEDpin, HIGH);
9. }
Arduino constants
The constants in Arduino are defined as the predefined expressions. It makes the code easy to read. The constants in Arduino are defined as:

## Slide 8
We can notice that the LEDpin is used both in the loop() and setup() functions. The value is used in both functions, so, changing the value in one function will reflect in the other. For example,
int LEDpin = 8;
void setup()
{
LEDpin = 13;
pinMode(LEDpin, OUTPUT);
}
7. void loop()
8. {
9. digitalWrite(LEDpin, HIGH);
10. }
Here, the value 13 will be passed to the digitalWrite() function.

## Slide 9
Arduino constants
The constants in Arduino are defined as the predefined expressions. It makes the code easy to read. The constants in Arduino are defined as:
Logical level Constants:
The logical level constants are true or false. The value of true and false are defined as 1 and 0.
Any non-zero integer is determined as true in terms of Boolean language. The true and false constants are type in lowercase rather than uppercase (such as HIGH, LOW, etc.).
Pin level Constants:
The digital pins can take two value HIGH or LOW. In Arduino, the pin is configured as INPUT
or OUTPUT using the pinMode() function. The pin is further made HIGH or LOW using the digitalWrite() function.

## Slide 10
HIGH. The board includes two types of voltage pins to provide HIGH value, which are listed below:
5V
3V
Some boards include only 5V pins, while some include 3.3V. Some boards consist of both 5V and 3.3V pins. For example, Arduino UNO R3. The pin configured as HIGH is set at either 5V or 3.3V.
The pins are configured at the 5V or 3.3V depending on:
for voltage > 3.0V (presented at 5V pin)
for voltage > 2.0V (presented at 3.3V pin)
LOW. The pin configured as LOW is set at 0 Volts. The pins are configured at the 5V or 3.3V depending on:
for voltage < 1.5V (presented at 5V pin)
for voltage < 1V (presented at 3.3V pin)

## Slide 11
LED_BUILTIN Constant
The Arduino boards have built-in LED connected in series with the resistor. The particular pin
number is defined with the constant name called LED_BUILTIN. Most Arduino boards have the LED_BUILTIN connected to Pin number 13.
Constant Keyword
The name const represents the constant keyword. It modifies the behavior of the variables in our
program. It further makes the variable as 'read-only'. The variable will remain the same as other variables, but its value cannot be changed. It means we cannot modify the constant.
For example,
const int a =2;
//....
3. a = 7; // illegal - we cannot write to or modify a constant

## Slide 12
The const keyword is considered superior compared to the #define keyword because it obeys the rules of the variable scope.
For example,
const float x = 5.68;
float y;
void setup()
{
Serial.begin(9600);
y = x * 2; // we can also use constants in math
Serial.println(y);
}
9. void loop()
10. {
11. // ....
Output: 11.36
Note: We can either use const or #define in the case of strings and numeric constants. But we can only use const for arrays.

## Slide 13
#define
The #define in Arduino is used to give a name to the constant value. It does not take any memory
space on the chip. At the compile time, the compiler will replace the predefined value in the program to the constants with the defined value.
The syntax is:
#define nameOFconstant value
where,
nameOFconstant: It is the name of the macro or constant to define
value: It includes the value assigned to the constant or macro. For example,
#define LEDpin 12
// It is the correct representation of #define
Note: The #define does not require any semicolon. Hence, we do not need to specify any semicolon after the #define. Otherwise, the compiler will show errors.

## Slide 14
The incorrect declarations of #define can be:
#define LEDpin = 12
#define LEDpin 12;
// both of the above statements are incorrect