## Slide 1
DISCOVER . LEARN . EMPOWER
Biosensors, principle and its types
UNIVERSITY INSTITUTE OF SCIENCES
Academic Unit V
Bachelor of Engineering
(Computer Science & Engineering)
Biology For Engineers

## Slide 2: Course Outcome
CO Number | Title | Level
CO1 | Identify the biological concepts from an engineering perspective. | Remember
CO2 | Development of artificial systems mimicking human action. | Understand
CO3 | Explain the basic of genetics that helps to identify and formulate problems | Understand
CO4 | Apply knowledge of measurement system, biomedical recording system and biosensors to excel in areas such as entrepreneurship, medicine, government, and education. | Understand
CO5 | Integrate biological principles for developing next generation technologies | 
Will be covered in this lecture
https://images.app.goo.gl/5obqqxo93P2UBmdU6

## Slide 3: SYLLABUS
Unit-2 | Biosensors and measurement system | Contact Hours: 15
Chapter 1 Medical Instrumentation Chapter 2 Measurement System Chapter 3 Biological Sensor | Medical Instrumentation: Sources of biomedical Signals, Basic medical Instrumentation system, Performance requirements of medical Instrumentation System, Microprocessors in Medical instruments, PC base medical Instruments, General constraints in the design of medical Instrumentation system, Regulation of Medical Devices. Measurement System: Specification of instruments, Statics & Dynamic characteristics of medical instruments, Classification of errors. Statistical analysis, Reliability, Accuracy, Fidelity, Speed of responses, Linearization of technique, and Data Acquisition System. Biological sensors: Sensors/ receptors in the human body, basic organization of the nervous system- neural mechanism, Chemoreceptor: hot and cold receptors, sensors for smell, sound, vision, Ion exchange membrane electrodes, enzyme, glucose sensors, immunosensors, & biosensors & applications of biosensors. | 

## Slide 4: Introduction of Biosensors

## Slide 5
Sensor
A sensor measures a physical quantity and converts it into a signal which can be read by an observer or by an instrument.
Transducer
A device that is capable of converting the physical quantity into a proportional electrical quantity such as voltage or current.

## Slide 6: Biosensor
A biosensor is an analytical device, used for the detection of an analyte, that combines a biological component with a physicochemical detector.
Containing an immobilized biological material (enzyme, nucleic acid, hormone, organelle or whole cell) which can specifically interact with an analyte and produce physical, chemical or electrical signals that can be measured.
An analyte is a compound (e.g. glucose, urea, drug, pesticide) whose concentration has to be measured.
  For instance, glucose is an 'analyte' in a biosensor designed to detect glucose.

## Slide 8: GENERAL FEATURES OF BIOSENSOR
Biosensors are devices comprising a biological element and a physiochemical detector that are used to detect analytes.
A biosensor has two components
Biological component: Biological element, analyte.
Physical component: Transducer, amplifier etc.
Biological component (Enzyme, cell etc.) recognizes and interacts with the analyte to produce a physical change (a signal) that can be detected, by the transducer.
Used to increase the power, voltage of a signal.
Convert one signal to electrical signal
Biological material
Compound- whose concentration measured

## Slide 9
Compound- whose concentration measured
Used to increase the power, voltage of a signal.
Process signal for display
Visual results
Biological signal>>electrical signal
Biological material

## Slide 10: Basic Principle of Biosensor
Basic principle of biosensor involved in three element :
Biological recognition element which highly specific towards the biological material analytes produces.
Transducers detect and transduces signal from biological target - receptor molecule to electrical signal which is due to reaction occur.
After transduction, signal from biological to electrical signal where its amplification is necessary and takes place and read out in detector after processing the values are displayed for monitor and controlling the system.

## Slide 11: Working Principle of Biosensor
The biological material is immobilized and a contact is made between the immobilized biological material and the transducer
The analyte binds to the biological material to form a bound analyte which in turn produces the biological response that can be measured.
Sometimes the analyte is converted to a product which could be associated with the release of heat, gas (oxygen), electrons or hydrogen ions.
The transducer measures this interaction and outputs a signal.
The intensity of the signal output is proportional to the concentration of the analyte.
The transducer then converts the product linked changes into electrical signals which can be amplified and measured by the electronic system.

## Slide 13
A substance of interest that needs detection
Chemical substance
Biological constituent
Glucose
Ammonia
Alcohol
Lactose
Metal ion
Protein
Toxin
Peptide
Vitamin
Antibody
The Analyte

## Slide 14
Bioreceptor
(Biological Element)
The component used to bind the target molecule
Microorganism
Must be highly specific, stable under storage conditions, and immobilized
Tissue
Cell
Organelle
Nucleic acid
Enzyme
Enzyme component
Receptor
Antibody

## Slide 15: Types of biosensors
Based on Transducer
Ion-sensitive biosensor
Calorimetric/Thermometric Biosensor
Electrochemical Biosensor
4. Wearable Biosensors

## Slide 16: 1. Ion Sensitive Biosensor
These are semiconductor FETs
Having an ion-sensitive surface (Selectively permeable to analyte ions).
Ions diffuse through layer, ,,,,,cause change in surface potential.
Change in the potential can be subsequently measured.
The Ion Sensitive Field Effect Transistor (ISFET) can be constructed by covering the sensor electrode with a polymer layer.
This type of biosensor is also called an ENFET (Enzyme Field Effect Transistor) and is primarily used for pH detection.
Notes: The field-effect transistor is a type of transistor that uses an electric field to control the flow of current in a semiconductor.
FETs are devices with three terminals: source, gate, and drain.

## Slide 17
2. Calorimetric/Thermometric Biosensor
Advantages:
No need of frequent recalibration (instrument check—whether working accurately).
Uses:
Detection of : Pesticides and Pathogenic bacteria
The reaction takes place in a small enzyme reactor.
As the substrate enters the bed, it gets converted to a product and heat is generated.
e.g: When cholesterol gets oxidized by the enzyme cholesterol oxidase, heat is generated which can be measured.
Temperature is measured by Thermistors.
This type of biosensor is used to measures the change in temperature

## Slide 18
3. Electrochemical Biosensor
Many chemical reactions produce or consume ions or causing some change in the electrical properties of the solution that can be sensed out & used as a measuring parameter.
Such types of rection are called Redox reactions
Electrochemical biosensors are classified into three types:
Amperometric Biosensors
Potentiometric Biosensors
Impedimetric Biosensors
Generally, the electrochemical biosensor is based on the reaction of enzymatic catalysis that consumes or generates electrons.

## Slide 19
4. Wearable Biosensors
Digital device, used to wear on the human body (like smart watches, smart shirts, tattoos which allows the levels of blood glucose, Blood Pressure, the rate of heartbeat).
Wearable biosensors (WBSs) are portable electronic devices that integrate sensors into/or with the human body

## Slide 20
Enzyme Biosensors
An enzyme biosensor is an analytical device that combines an enzyme with a transducer to produce a signal proportional to target analyte concentration.
Because of their specificity and catalytic properties, enzymes have found widespread use as sensing elements in biosensors.

## Slide 21
Enzymes are proteins that help speed up metabolism, or the chemical reactions in our bodies. They build some substances and break others down. All living things have enzymes. Our bodies naturally produce enzymes.
ENZYMES
CLASSIFICATION OF ENZYMES/ TYPES with e.g
OTHLIL

## Slide 23
Glucose Sensors
Designed to detect glucose levels, which is vital to managing diabetes.
Whether in the form of a test strip of blood glucose meter or a sensor for a continuous glucose monitor, the detection and measurement of glucose levels are similar processes.
For a glucose biosensor, the following components are used:
Analyte: glucose is the analyte that the biosensor is designed to detect.
Bioreceptor: The test strip for a blood glucose test contains the enzyme that interacts with the analyte in the drop of blood.

## Slide 24: Glucose Sensors
Transducer: Convert biochemical signals into electrical signals.
Electronics and display: The processed signals are then quantified and shown on either the glucose meter’s display or the receiver for a continuous glucose monitor (or compatible app).

## Slide 25
Analyte (Glucose) + Enzyme (Glucose oxidase)----Gluconic acid----------measured and displayed
Convert signals
Recognize analyte
Chemical being identified and measured
Biological system + Instrument (Biosensor)
Bio signals
e.g. of Biosensor- GULUCOSE BIOSENSOR

## Slide 26
Higher the glucose content, the higher gluconic acid------more reading or value.
Glucose reacts with glucose oxidase to form gluconic acid.

## Slide 27
Immunosensors
Immunosensors are affinity ligand-based biosensing devices that involve the coupling of immunochemical reactions to appropriate transducers.
Immunosensors use antibodies as the recognition element and a transducer that converts the antibody–antigen binding event to a measurable physical signal.

## Slide 28
Analyte:
Antigen
Bioreceptor:
Antibody
Antigen is a substrate that stimulates the immune system to produce antibodies.
Antibodies are Y- shaped proteins formed in response to any foreign substance known as an antigen
Transducer:
Electrochemical, optical and thermometric
Electronics and display:
The processed signals are then quantified and shown on display
Convert signal

## Slide 29: Applications of Biosensors
Biosensor devices include a biological element as well as a physiochemical detector and the main function of this device is to detect analytes.
These devices are applicable in the medical, food industry, the marine sector as they offer good sensitivity & stability as compared with the usual techniques.
In recent years, these sensors have become very popular, and they are applicable in different fields.

## Slide 31: Applications of Biosensors/ Immunosensor utilized in medical app?
Some examples of the fields that use biosensor technology include:
  General healthcare monitoring
  Medical Diagnosis
  Metabolites Measurement
  Screening for disease
  Clinical analysis and diagnosis of disease
  Drug development and improvement
  Veterinary and agricultural applications
  Industrial processing and monitoring
  Environmental pollution control
  Study & Interaction of Biomolecules
  Detection of Crime
  Quality Control

## Slide 32
Common Applications of Biosensors
Biosensors are used in the food industry to measure carbohydrates, alcohols and acids, for example, during quality control processes.
The devices may also be used to check fermentation during the production of beer, yoghurt and soft drinks.
Another important application is their use in detecting pathogens in fresh meat, poultry or fish.
Biosensors are used to check the quality of air and water.
The devices can be used to pick up traces of organophosphates from pesticides or to check the toxicity levels of wastewater

## Slide 33: REFERENCES
C.B.Powar, 2010.Cell Biology.5th Ed,Himalyan Publishing House.
Leshie Cromwell, Fred.J. Weibell and Erich.A.Pfeiffer. 2003. Biomedical instrumentation and measurements. 2nd edition, PHI.
John G. Webster 1998. Medical Instrumentation: Applications and Design, 3rd edition, Jon Wiley and Sons, New York.
Jeremy M. Berg, John L. Tymoczko and Lubert Stryer. 2006. “Biochemistry,” 6th Ed. W.H. Freeman and Co. Ltd.
Robert Weaver. 2012 “Molecular Biology,” 5th Edition, MCGraw-Hill.
Jon Cooper, , 2004. “Biosensors A Practical Approach” Bellwether Books.
Martin Alexander, 1994 “Biodegradation and Bioremediation,” Academic Press.

## Slide 34
THANK YOU