## Slide 1
Signal conditioners
Preamplifiers
Differential Amplifier
Isolation Amplifier
DISCOVER . LEARN . EMPOWER
UNIVERSITY INSTITUTE OF SCIENCES
Academic Unit V
Bachelor of Engineering
(Computer Science & Engineering)
Biology For Engineers
23SZT148

## Slide 2: Course Outcome
CO Number | Title | Level
CO1 | Identify the biological concepts from an engineering perspective. | Remember
CO2 | Development of artificial systems mimicking human action. | Understand
CO3 | Explain the basic of genetics that helps to identify and formulate problems | Understand
CO4 | Apply knowledge of measurement system, biomedical recording system and biosensors to excel in areas such as entrepreneurship, medicine, government, and education. | Understand
CO5 | Integrate biological principles for developing next generation technologies | 
Will be covered in this lecture
https://images.app.goo.gl/5obqqxo93P2UBmdU6

## Slide 3: SYLLABUS
Unit-3 | Bio Medical Instrumentation | Contact Hours: 15
Chapter 1 Electrical stimulus and biophysical activity Chapter 2 Biomedical recording system Chapter 3 Tissue Engineering | Electrical stimulus and biophysical activity: Patient, electrical shock and hazards, leakage current, Electrical activity of heart (ECG), Electrical activity of brain (EEG), Electrorentinogram (ERG), Electro-occologram (EOG), Electromyogram (EMG). Biomedical recording systems: Basic Recording system, General consideration for signal conditioners Preamplifiers, Differential Amplifier, Isolation Amplifier, Vectorcardiograph, Phonocardiograph, Other biomedical records, Patient isolation, and accident prevention. Tissue Engineering: Recombinant DNA technology, Stem cell biology & Tissue Engineering. | 

## Slide 4: Basic Recording System
Signal conditioners
Preamplifiers
Differential Amplifier
Isolation Amplifier

## Slide 5
Biomedical Recording Systems
Recorders provide permanent visual trace or record of an applied electrical signal.
The most basic electronic recording system consists of 3 important components:
Electrodes/Transducer
Signal conditioner
Writing system
The signal conditioner converts the output of the electrode/transducer into an electrical quantity suitable for operating the writing system.
The writing system provides a visible graphic representation of the quantity of the physiological variable of interest.
The electrode picks up the bioelectric potentials whereas the transducer converts the physiological signal to be measured into a usable electrical output.

## Slide 6
In medical recorders, the signal conditioner usually consists of a preamplifier and the main amplifier.
Both of these amplifiers must satisfy specific operation requirements such as input impedance, gain and frequency response characteristics for an effective reproduction of the input signal.
To make the signal from any transducer compatible with the input signal required for the driver amplifier of the display or recording system, it is usual to arrange to normalize the electrical signals produced by each transducer.
This is done in the signal conditioner which adjusts its output to a common signal level e.g. one volt.
The necessary adjustments of gain and frequency response are provided by the signal conditioners.
This means that, it is possible to interchange the signal conditions to record any one of the physical or bioelectric events on the same writing channel.
The writing systems which are available in many forms constitute the key portion of the recording instrument.
Examples of commonly used writing system include: The Inkjet recorder, Galvanometer type pen recorder, Potentiometric recorder, etc.

## Slide 7
What is Signal Conditioning?
Analog signals need to be correctly "prepared" before they can be converted into digital form for further processing.
For example, thermocouple signals have very small voltage levels that must be amplified before they can be digitized.
Signal conditioning is one of the fundamental building blocks of modern data acquisition (aka DAS or DAQ system).
Signal conditioning is an electronic circuit that manipulates a signal in a way that prepares it for the next stage of processing.
Many data acquisition applications involve environmental or mechanical measurement from sensors, such as temperature and vibration. These sensors require signal conditioning before a data acquisition device can effectively and accurately measure the signal.
Other sensors, such as resistance temperature detectors (RTDs), accelerometers, and strain gauges require excitation to operate.
All of these preparation technologies are forms of signal conditioning.
The basic purpose of a data acquisition system is to make physical measurements.

## Slide 8
Top Requirements of Signal Conditioners
Today signal conditioners include some of the required elements that make them useful for modern data acquisition systems. These elements are:
Electrical isolation
The right connectors for sensor connections
Measurement range selection
Signal filtering (e.g. anti-aliasing filtering)
Conformance with sensor requirements.

## Slide 9
Biological Amplifiers
Generally, biological/bioelectric signals have low amplitude and low frequency.
Therefore, to increase the amplitude level of biosignals amplifiers are designed.
The outputs from these amplifiers are used for further analysis and they appear as ECG, EMG, or any bioelectric waveforms.
Such amplifiers are defined as Bio Amplifiers or Biomedical Amplifiers.

## Slide 10
Basic Requirements for Biological Amplifiers
The biological amplifier should have a high input impedance value. The range of value lies between 2 MΩ and 10 MΩ depending on the applications. Higher impedance value reduces distortion of the signal.
When electrodes pick up biopotentials from the human body, the input circuit should be protected. Every bio-amplifier should consist of isolation and protection circuits, to prevent the patients from electrical shocks.
Since the output of a bioelectric signal is in millivolts or microvolt range, the voltage gain value of the amplifier should be higher than 100dB.
Throughout the entire bandwidth range, a constant gain should be maintained.
A bio-amplifier should have a small output impedance.
A good bio-amplifier should be free from drift and noise.
Common Mode Rejection Ratio (CMRR) value of amplifier should be greater than 80dB to reduce the interference from common mode signal.
The gain of the bio-amplifier should be calibrated for each measurement.

## Slide 11
Preamplifier
A preamplifier, also known as a preamp, is an electronic amplifier that converts a weak electrical signal into an output signal strong enough to be noise-tolerant and strong enough for further processing.
Basically preamplifier is used for stabilizing effect.
The primary function of a preamplifier is to extract the signal from the detector without significantly degrading the intrinsic signal-to-noise ratio. Without this, the final signal would be noisy or distorted.
Therefore, the preamplifier is located as close as possible to the detector, and the input circuits are designed to match the characteristics of the detector.
An ideal preamp will be linear (have a constant gain through its operating range), have high input impedance (requiring only a minimal amount of current to sense the input signal) and a low output impedance (when current is drawn from the output there is minimal change in the output voltage).
Three basic types of preamplifiers are available:
Current-sensitive preamplifier
Parasitic-capacitance preamplifier
Charge-sensitive preamplifier.

## Slide 12
Differential Amplifier
Differential Amplifier is an important building block in integrated circuits of analog system.
Differential amplifier will reject any common mode signal that appears simultaneously at both amplifier input terminal and amplifies only the voltage difference that appears across its input terminals.
It typically forms input stages of operational amplifiers.
A differential amplifier (also known as a difference amplifier or op-amp subtractor) is a type of electronic amplifier that amplifies the difference between two input voltages but suppresses any voltage common to the two inputs.
In simple words, we can say it is a device that amplifies the difference of 2 input signals.
e.g. Buffer amplifier converts low impedance signals to high impedance signals.

## Slide 13
Isolation Amplifier
Isolation amplifiers are a form of differential amplifier that allow measurement of small signals in the presence of a high common mode voltage by providing electrical isolation and an electrical safety barrier.
An isolation amplifier increases the input impedance of a patient monitoring system.
Using the isolation amplifier prevents accidental internal cardiac shock.
It also helps to isolate the patient from the device.
Isolation amplifiers are used in medical instruments to ensure isolation of a patient from power supply leakage current.
It provides up to 1012 Ω insulation between the patient and the power line in the hospital.
These amplifiers are also used for amplifying low-level signals in multi-channel applications.
They can also eliminate measurement errors caused by ground loops. Amplifiers with internal transformers eliminate external isolated power supply.
They are usually used as analogue interfaces between systems with separated grounds.

## Slide 14: Biomedical Records
Vectorcardiograph
Phonocardiograph
Ballistocardiograph
Pulse Oximeter

## Slide 15
Vectorcardiograph
Vectorcardiography (VCG) is a method of developing two-dimensional (2D) images of cardiac electrical activity by displaying the spatial locations of ECG waveforms at each sequential time of their duration.
Vectorcardiograph is an instrument that record the magnitude and direction of the electrical forces that are generated by the heart by means of a continuous series of vectors that form curving lines around a central point.
The method was developed by E. Frank in the mid 1950s.
Since the human body is a three-dimensional structure, the basic idea is to construct 3 orthogonal leads containing all the electric information scanned in three mutually orthogonal axes (vertical, transversal, and sagittal).
Notes: Sagittal: of or in a plane parallel to the sagittal suture, especially that dividing the body into left and right halves.

## Slide 17
Vectorcardiography (VCG) is an investigation method that was previously compared to ECG several times and was evaluated as a useful investigation method.
VCG provides better sensitivity, for example for the detection of myocardial infarction, ischemia, and hypertrophy.
A Polaroid camera photographs the oscilloscope screen to provide a permanent record.
It is the recording of the moment-to-moment electromotive forces of the heart on a plane of the body surface delineated as a vector function of time.
With the modern computer facilities, the vectorcardiography may be clinically used in an extensive manner, even though it is not widely used clinically now.
It achieved a higher sensitivity for the detection of hypertrophy as well as ischaemic heart disease.
The vector cardiogram appears as loops in each plane.
There are three loops corresponding to P, QRS and T waves. Among this the QRS complex loop is dominating one.
However, in clinical practice, measurement of VCG is not usually used because it requires additional electrodes placed on the patient’s body.
Notes: Ischemic heart disease: It's the term given to heart problems caused by narrowed heart arteries.

## Slide 18
Phonocardiograph
Phonocardiography, diagnostic technique that creates a graphic record, or phonocardiogram, of the sounds and murmurs produced by the contracting heart, including its valves and associated great vessels.
The phonocardiogram is obtained either with a chest microphone or with a miniature sensor in the tip of a small tubular instrument that is introduced via the blood vessels into one of the heart chambers.
The phonocardiogram usually supplements the information obtained by listening to body sounds with a stethoscope (auscultation) and is of special diagnostic value when performed simultaneously with measurement of the electrical properties of the heart (electrocardiography) and pulse rate.
The device monitors the heart activity in terms of sound instead of electrical signals in an electrocardiograph.

## Slide 19
The phonocardiogram (PCG) detects and records heart sounds, the sounds made by the various cardiac structures pulsing and moving blood.
In phonocardiography the second heart sound is important in appraisal of congenital heart disease and pulmonary hypertension because it reflects the duration of right ventricular systoles.
Heart sounds are diagnostically useful as they provide valuable information regarding certain types of heart disorders associated with the beating of the heart and the pumping action of the blood.
Congenital heart defects or acquired heart valve diseases are frequently the source of abnormal heart murmurs.
The sound is caused by the acceleration and deceleration of blood and turbulence developed during rapid blood flow.
Reference tracings in phonocardiography are useful for showing the interrelationship of the various cardiac sounds and murmurs.
Heart murmurs are generated as a result of turbulence in blood flow through narrow cardiac valves or reflow through the atrioventricular valves.

## Slide 20
PCG is an instrument used for recording waveforms of the heart sounds.
These wave-forms are diagnostically more important information revealing more than the heart sounds themselves.
The principal instrument used for detection of heart sounds is the acoustical stethoscope.
Air-coupled microphone and contact microphone are commonly in use for recording phonocardiograms.
PCG offers an additional valuable tool in primary clinical diagnosis and in cardiac monitoring functions.
The technique is particularly useful in foetal monitoring.
An improvement over the acoustical stethoscope is the electronic stethoscope consisting of a microphone, amplifier and headset.

## Slide 21
Ballistocardiograph
Ballistocardiograph is a device for measuring the amount of blood passing through the heart in a specified time by recording the recoil movements of the body that result from contraction of the heart muscle in ejecting blood from the ventricles.
Any approach for capturing forces generated by the body can be termed ballistography (BSG) and includes forces due to body movement, breathing motion and the mechanical action of the beating heart (also called ballistocardiography, BCG).
Ballistocardiograph is an instrument that records the movement imparted to the body with each beat of the heart cycle.
Ballistocardiogram (BCG) is a non-invasive technique to measure cardiac parameters.
It was popularized by Dr. Isaac Staar in 1940.
Abnormality appearing in the BCG may indicate about Coronary artery disease.
Notes: A ballistic body is a free-moving body with momentum which can be subject to forces such as the forces exerted by pressurized gases from a gun barrel or a propelling nozzle, normal force by rifling, and gravity and air drag during flight.

## Slide 22
The ballistocardiograph (BCG) is a measure of ballistic forces generated by the heart.
The heartbeat results in motion of the body, which in turn causes movements in a suspended supporting structure, usually a special table or bed on which the subject is lying, and these movements are recorded photographically (ballistocardiogram, or BCG) as a series of waves.
Ballistocardiograph is an instrument that records the movement imparted to the body with each beat of the heart cycle.
These movements occur during the ventricular contractions of the heart muscle when the blood is ejected with sufficient force.
Ballistocardiography, graphic recording of the stroke volume of the heart for the purpose of calculating cardiac output.

## Slide 23
The BCG is one of the most sensitive measures of the force of the heartbeat, and an abnormality appearing in the BCG of an apparently healthy subject aged 40, or younger, may be suggestive of symptomatic coronary disease.
The validated model reveals that the principal mechanism for the genesis of the BCG waves is blood pressure gradients in the ascending and descending aorta.
This new mechanistic insight may be exploited to allow BCG to realize its potential for unobtrusive monitoring and diagnosis of cardiovascular health and disease.

## Slide 24
Pulse Oximeter
Pulse oximetry is a noninvasive test that measures the oxygen saturation level of your blood.
It uses light beams to estimate the oxygen saturation of the blood and the pulse rate.
It can rapidly detect even small changes in oxygen levels.
The pulse oximeter is a small, clip-like device that is usually placed on a fingertip.
These levels show how efficiently blood is carrying oxygen to the extremities furthest from your heart, including your arms and legs.
Oxygen saturation gives information about the amount of oxygen carried in the blood.

## Slide 25
The pulse oximeter can estimate the amount of oxygen in the blood without having to draw a blood sample.
The principle of operation of pulse oximeter is based on the concept that the arterial oxygen saturation determinations can be made using two wavelengths.
The instrument consists of a pair of small LEDs facing a photodiode (photosensor).
The light from the LEDs, passes through a translucent part of the patient’s body generally forefinger.
These two wavelengths assume two absorbers namely: Oxyhaemoglobin (HbO2) and Haemoglobin (Hb).
One of these two LEDs transmits infrared light at a wavelength of approximately 940 nm while the other transmitting light at approximately 660 nm.

## Slide 26
The pulse oximeter operates on the principle of absorption of light by the solutes in a solution.
The Beer-Lambert law states that the amount of light absorbed by a solute is proportional to the concentration of the solute and the distance the light is transmitted through the solution.
The absorption of these select wavelengths of light through living tissues is significantly different for oxygenated haemoglobin (HbO2) and reduced haemoglobin (Hb).
In the red part of the spectrum, oxygenated haemoglobin absorbs less light than deoxygenated haemoglobin, while the reverse occurs in the infrared region.
The absorption of these selected wavelengths of light passing through living tissue is measured with a photodiode/photosensor.
The output of the photodiode will have one signal that represents the absorption of red light (660 nm) and other signal that represents infrared light (940 nm).
The oxygen saturation is estimated from the Ratio (R) of pulse-added red absorbance at 660 nm to the pulse-added infrared absorbances at 940 nm.
Oxygen saturation values are between 95% and 100% for most healthy individuals.

## Slide 27: REFERENCES
John G Webster, “Medical Instrumentation – Application and Design”, 4th ed., John Wiley and Sons, 2007.
Leslie Cromwell, Fred. J. Weibell, Erich. A. Pfeiffer, “Biomedical Instrumentation & Measurements, 2nd ed., Pearson Education., 2001.
Basmajian, “Biofeedback- Principles and practice for clinicians.”
Susan o Sullivan, “Physical rehabilitation”
Ryaby J.T. (2005) Biophysical Stimulation Using Electrical, Electromagnetic, and Ultrasonic Fields. In: Lieberman J.R., Friedlaender G.E. (eds) Bone Regeneration and Repair. Humana Press. https://doi.org/10.1385/1-59259-863-3:291
Leshie Cromwell, Fred.J. Weibell and Erich.A.Pfeiffer. 2003. Biomedical instrumentation and measurements. 2nd edition, PHI.
John G. Webster 1998. Medical Instrumentation: Applications and Design, 3rd edition, Jon Wiley and Sons, New York.
Jon Cooper, , 2004. “Biosensors A Practical Approach” Bellwether Books.

## Slide 28
THANK YOU