## Slide 1
DISCOVER . LEARN . EMPOWER
FIBRE OPTICS
INSTITUTE :UIE
DEPARTMENT: ALL ACADEMIC UNITS
Bachelor of Engineering (All Sections)
Subject Name and Code:
Engineering Physics 23SPH-141
Prepared by: Deepak Kumar, Asso. Prof. Physics

## Slide 2
The course is designed to make the students industry ready to contribute in the growing demand of the industry at local, national and international level.
It will make the students competent to understand basic concepts and applications of advanced engineering physics and apply its principles in their respective fields at global platform.
It will enhance the skill level of the students and shall make them preferred choice for getting employment in industry and research labs.
It will give thorough knowledge of the discipline to enable students to disseminate knowledge in pursuing excellence in academic areas.
Course Objectives

## Slide 3
Course Outcomes
Figure 2.1 Optical fibres [1]
CO Number | Title On completion of this course, the students are expected to learn | Level
CO1 | Quote the basic fundamental concepts of lasers, optical fibres, crystallography, ultrasonic oscillations, semiconductor physics, quantum mechanics and nanotechnology. | Remember, Understand
CO2 | Demonstrate the working of various lasers, fibre components, semiconductor devices; explain the behaviour of crystalline solids, quantum and nano-scale systems. | Understand
CO3 | Solve problems by applying principles related to lasers, fibres, semiconductors, oscillations, quantum and nanoscience. | Applying
CO4 | Compare various lasers and fibres, semiconducting devices, crystalline materials, structures at quantum and nanoscale on the basis of their properties for industrial applications. | Analyze
CO5 | Develop various systems using lasers, fibres, semiconductors and nanomaterials for futuristic applications. | Design

## Slide 4: Brief Flow of Presentation
Brief Introduction
Optical fiber construction
Critical angle & Total Internal Reflection
Acceptance angle & acceptance cone
Numerical Aperture
V-Number
Types of fibers
Dispersion & its types
Attenuation and Losses in Fiber
Advantages
Disadvantages
Applications
Figure 2.2 Basic structure and parts of optical fibre [2]

## Slide 5: Definition of Optical fiber
An optical fiber is a flexible, transparent fiber made by glass (silica) or plastic to a diameter slightly thicker than that of a human hair.
Optical fiber is a dielectric waveguide and ideally has a cylindrical shape.
It consists of a core made up of a dielectric material which is surrounded by a cladding made up of a dielectric material of lower refractive index than core.

## Slide 6
Core
Cladding
Buffering
Core having higher refractive index than cladding
Figure 2.3 Parts of optical fiber [3]
Parts of Optical Fiber

## Slide 7
Core – thin glass center of the fiber where light travels.
Cladding– outer optical material surrounding the core.
Buffer Coating- plastic coating that
protects the fiber.

## Slide 8: FIBER MANUFACTURE
I- Glass-Glass Fiber
Glass as silica (SiO2) with refractive Index (RI) of 1.458 at 850nm
Addition of GeO2 and P2O5 increases RI.
Addition of B2O3 and fluorine decreases RI.
Figure 2.4 Increase or decrease of RI by adding dopants [4].

## Slide 9: FIBER MANUFACTURE
II- Plastic clad Glass Fiber
Glass core and plastic cladding.
Higher losses.
Short distance (several hundred meters).
Reduced cost.
Core Silicon resin RI = 1.405 at 850nm
Clad is Teflon PEP (Perfluoronated ethylene propylene) with RI = 1.338.
Large NA with large RI difference.
Core dia of 150 to 600µm.
LED as source.
I- Glass-Glass Fiber
Combinations can be—
GeO2 - SiO2 core, SiO2 Cladding.
P2O5 - SiO2 core, SiO2 Cladding.
SiO2 core, B2O3 -SiO2 Cladding.
GeO2 - B2O3 - SiO2 core, B2O3 -SiO2 Cladding.

## Slide 10: FIBER MANUFACTURE
Remember!
Germanium dioxide and phosphorus pentaoxide increase the refractive index of glass
Boron oxide decreases the refractive index of glass.
These oxides are known as dopants.
Changing composition of the mixture during the process influences refractive index profile of the preform
III- Plastic Fiber
Very short distance (100m max).
High attenuation.
Low cost, tough, durable, inexpensive.
Core dia of 110 to 1400µm.
LED as source.
Polystyrene core (1.6), methyl methacrylate clad (1.49). NA = 0.6.
Polymethyl methacrylate core(1.49), its co-polymer(1.40), NA = 0.5

## Slide 11: Transmission of Light Through Optical Fibers
Its total Internal Reflection
(a)
Figure 2.5 (a) & (b) Diagram of total internal reflection in different type of optical fiber [5].
(b)

## Slide 12: Ray Theory Transmission
Refractive index
The index of refraction of a material is the ratio of the speed of light in a vacuum to the speed of light in the material
n = c/v
The factor n is the index of refraction (or refractive index) of
the medium.
For air and gases n ~ 1. At optic frequencies, the refractive index of water is 1.33.
Glass has many compositions, each with a slightly different
n. An approximate refractive index of 1.5 is representative for the silica glasses used in fibers; more precise values for these glasses lie between ~1.45 and ~1.48.

## Slide 13: Ray Theory Transmission

## Slide 14: Critical Angle (c)
The angle at which total internal reflection occurs is called the critical angle of incidence.
At any angle of incidence (1) greater than the critical angle, light is totally reflected back to the glass medium.
For n1 > n2, the angle of refraction 2 is always greater than the angle of incidence 1.
When the angle of refraction 2 is 90o the refracted ray emerges parallel to the interface between the media.

## Slide 15: Total internal reflection
At angles of incidence 1 > c the light is totally reflected back into the incidence higher refractive index medium. This is known as total internal reflection.

## Slide 16
Air -----------------------------------------------------------------------1.00
Water --------------------------------------------------------------------1.33
Magnesium fluoride --------------------------------------------------1.38
Fused silica (SiO2)-----------------------------------------------------1.46
Sapphire (Al2O3)-------------------------------------------------------1.80
Lithium niobate (LiNbO3)--------------------------------------------2.25
Indium phosphide (InP)----------------------------------------------3.21
Gallium arsenide (GaAs) ---------------------------------------------3.35
Silicon (Si)---------------------------------------------------------------3.48
Indium gallium arsenide phosphide (InGaAsP)-----------------3.51
Aluminum gallium arsenide (AlGaAs)-----------------------------3.60
Germanium (Ge) -------------------------------------------------------4.00
  The index varies with a number of parameters, such as wavelength and temperature.
Refractive Index of Some Materials

## Slide 17: Assessment Test
Quiz link for Assessment Test:-
https://docs.google.com/forms/d/e/1FAIpQLSdoaR30UPyyOY0IRVyChKPoZVB99BOTYyw61SPEVbYoxNepFQ/viewform?usp=pp_url
Home Assignment :-
Q.1 Why silica is used for the fabrication of the optical fibers?
Q.2 What is the principle of fiber optical communication?
Q.3 Do signals really travel faster in fiber optics?
Q.4 What is a better way of communication, wire or fiber optics?

## Slide 18: References
[1] https://www.ispreview.co.uk/index.php/2013/07/alcatel-lucent-breaks-record-with-31tbps-over-a-single-fibre-optic-cable.html
[2] http://constructionmanuals.tpub.com/14026/css/Fiber-Buffers-193.htm
[3] https://www.slideshare.net/ankushsaini123/6796optical-fibres
[4] https://www.slideshare.net/MadhumitaTamhane/optical-fiber-communication-part-1- optical-fiber-fundamentals
[5] (a) http://constructionmanuals.tpub.com/14026/css/Fiber-Buffers-193.htm
(b) https://computer.howstuffworks.com/fiber-optic2.htm
[6] https://www.slideshare.net/PratyushSrivastava8/optical-fiber-cable- v2?from_action=save
[7] https://www.ques10.com/p/21598/derive-the-expression-of-numerical-aperture- for-a-/
[8] https://www.explainthatstuff.com/fiberoptics.html
[9] http://fiberonda.com/single-mode-vs-multi-mode-fiber-optic-cable/
[10] https://images.app.goo.gl/LLWfgV3PjgLc9RbDA

## Slide 19
Text book
Beiser A., Ghatak A, Garg S.C., Applied Physics, Edition 1st, (2013), Tata McGraw-Hill, Noida.
Laud B.B., Laser and Non -Linear Optics, Edition 1st, (1991), Wiley Eastern Ltd.
E- content
http://www.fiberopticshare.com/what-are-the-components-of-optical-fiber.html

## Slide 20
THANK YOU
For Queries:-
deepak.e1972@cumail.in