## Slide 1
DISCOVER . LEARN . EMPOWER
Logic Gates
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code- 23ECH-101
Prepared By
Dr. Shikha
Unit-1 Chapter-2
Introduction of Electrical & Electronics Circuit
Lecture No. 1.2.4

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about different logic gates
2 | To impart knowledge about realizing a logic function using gates.
3 | To make and understand of deriving basic gates from universal gates.

## Slide 3: Course Objectives
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4: Course Outcomes
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 5: LOGIC GATES
  Logic gates
  Realization of circuit using gates
Figure 1.2 Classification of logic Gates [5]

## Slide 6: NOT LOGIC GATE
NOT gate has only one input and one output
IC used for two input NOT gate is 7404 .
A (input) | Y (output)
0 | 1
1 | 0
Figure 1.5 Symbol of NOT gate [12 ]
Truth Table of NOT gate
Boolean Expression : Y = Aꞌ
Figure 1.6 NOT GATE[2]

## Slide 7: AND LOGIC GATE
And gate has n no. Of inputs and one output whereas in the symbol there are only two inputs.
IC used for two input AND gate is 7408 .
A (input) | B(input) | Y (output)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Figure 1.3 Symbol of AND gate [12]
Truth Table of AND gate
Boolean Expression : Y=A.B

## Slide 8: OR LOGIC GATE
OR gate has n no. Of inputs and one output whereas in the symbol there are only two inputs.
IC used for two input OR gate is 7432 .
A (input) | B(input) | Y (output)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Figure 1.4 Symbol of OR gate [12 ]
Truth Table of OR gate
Boolean Expression : Y=A + B

## Slide 9: NAND LOGIC GATE
NAnd gate has n no. Of inputs and one output whereas in the symbol there are only two inputs.
IC used for two input NAND gate is 7400 .
A (input) | B(input) | C (output)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Figure 1.6 Symbol of NAND gate [12 ]
Truth Table of NAND gate
Boolean Expression : Y= A.B

## Slide 10: NOR LOGIC GATE
NOR gate has n no. Of inputs and one output whereas in the symbol there are only two inputs.
IC used for two input NOR gate is 7402 .
A (input) | B(input) | Y (output)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Figure 1.7 Symbol of NOR gate [12 ]
Truth Table of NOR gate
Boolean Expression : Y= A + B

## Slide 11: EX-OR LOGIC GATE
XOR gate has n no. Of inputs and one output whereas in the symbol there are only two inputs.
IC used for two input XOR gate is 7486 .
A (input) | B(input) | Y (output)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Figure 1.8 Symbol of XOR gate [12 ]
Truth Table of XOR gate
Boolean Expression : Y=A B
⊕

## Slide 12
BASIC GATES FROM UNIVERSIAL GATES
  AND gate using NAND gate
  OR gate using NAND gate.
Figure 1.9 conversion of AND gate from NAND Gate [8]
Figure 1.10 conversion of OR gate from NAND Gate [8]

## Slide 13: BASIC GATES FROM UNIVERSIAL GATES
  NOT gate using NAND gate
  XNOR gate using NAND gate
  XNOR gate using NAND gate
Figure 1.11 conversion of NOT gate from NAND Gate [8]
Figure 1.12 conversion of XNOR gate from NAND Gate [8]
Figure 1.9 conversion of XOR gate from NAND Gate [8]

## Slide 14: APPLICATIONS
Computers
Calculators
ATM
Mobile Phone
Integrated Circuits and so on......

## Slide 15: REFERENCES
https://www.vivaxsolutions.com/physics/allogicgates.aspx
https://www.androiderode.com/ttl-not-gate/
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.
http://www.geeksforgeeks.org/digital-electronics-logic-design-tutorials/
http://www.ni.com/example/14493/en/
http://195.134.76.37/applets/AppletGates/Appl_Gates2.html
https://www.javatpoint.com/and-gate-in-digital-electronics
https://www.allaboutcircuits.com/textbook/digital/
https://www.tutorialspoint.com/digital_electronics/index.asp
https://www.tutorialspoint.com/computer_logical_organization/complement_arithmetic.htm

## Slide 16
THANK YOU