## Slide 1
DISCOVER . LEARN . EMPOWER
K-MAP
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code-23ECH-101
Prepared By
Dr. Shikha
Unit-1 Chapter-3
Basics of Electrical & Electronics Circuit
Lecture No. 1.3.6

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about K-map formation.
2 | To impart knowledge about simplification of SOP and POS expressions using K-Map.
3 | To make and understand the concept of do not care terms and their role in logic simplification.

## Slide 3: Course Objectives
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4: Course Outcomes
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 5: Karnaugh Map
  K map
  Simplification using K map
    SOP Form & POS form
    Don’t care
Boolean expression representation
Y= AB’C+ABCD’+AC’D’
Y = (A+B’) (A’+B+D’)(A+D’)

## Slide 6: Karnaugh maps (K-maps) are graphical method for the simplification of Boolean functions. K- maps consists of cells Cells = 2n where n = no of i/p variables. K-map cells are arranged so that adjacent cells differ in only one bit position (based on gray code).
K- maps
Figure 1.2 cells of k-map [2]

## Slide 7
Input Variables | K map for SOP form | K map for POS
2 (AB) |  | 
3(ABC) |  | 
4 (ABCD) |  | 

## Slide 8
Draw the Karnaugh map depending on variables as given in question.
Identify minterms (SOP ) and Maxterms (POS) as given in problem.
For SOP put 1’s in blocks of K map according to minterms.
For POS put 0’s in blocks of K map according to maxterms.
Make groups/pairs containing total terms in power of 2 like (2,4,8,16) Try to make the largest possible pair.
Find product terms with variables (that are unchanged along rows and columns ) for each group and sum up for SOP form.
Find sum terms with variables (that are unchanged along rows and columns ) for each group and ANDED them for POS form.
Steps to solve expression using K-map

## Slide 9: Pairing Rules of K-map
Adjust cells can be paired.
Corner elements can be paired . 3. outermost rows as well as outermost columns can be paired respectively.
4. Try to make largest possible pair as shown.

## Slide 10
5. Groups may overlap. 6. Diagonal pair is not possible.
7. Make sure in each pair ,there must be one unpaired 1(sop) or 0(pos) .
Pair in brown colour is not possible as it does not contain any unpaired 1.

## Slide 11: Questions on K- Maps (SOP)
Example: Simply F(A,B,C) = ∑ m( 1,3,4,5,7) using K – map and realize the circuit using AOI gates.
(a) K-map
Output Expression : F= AB’ + C
(b) Realization using gates.
Notes: This slide is animation based so view it in slide show mode for better understanding and colour of pairing in the k-map resembles the colour of corresponding term in the expression to avoid confusion.

## Slide 12: Questions on K- Maps( SOP )
Example: Simply F(A,B,C,D) = ∑ m( 2,3,8,10,11,12,14,15) using K – map and realize the circuit using AOI gates.
Output Expression : F= AC + AD’ + B’C
(b) Realization using gates.
(a) K-map
Notes: This slide is animation based so view it in slide show mode for better understanding and colour of pairing in the k-map resembles the colour of corresponding term in the expression to avoid confusion.

## Slide 13: Questions on K- Maps (POS)
Example: Simply F(A,B,C,D) = ∏M( 0,1,2,4,6,8,9) using K – map and realize the circuit.
(a) K-map
(b) Realization using gates.
Output Expression : F= (A+D) (B+C)
Notes: This slide is animation based so view it in slide show mode for better understanding and colour of pairing in the k-map resembles the colour of corresponding term in the expression to avoid confusion.

## Slide 14: K-map with Don’t care conditions:
Example: Simply F(A,B,C,D) = ∑m( 1,5,6,12,13,14)+d(4) using K – map.
(a) K-map
Output Expression : F=BD’+ A’C’D + BC’
(b) Realization using gates.

## Slide 15: K-map with Don’t care conditions:
Example: Simply F(A,B,C,D) = ∏M(3,9,12,15)+Փ(1,11,13,14) using K – map and realize the circuit.
(a) K-map
Output Expression : F=(B+D’) (A’+B’)
(b) Realization using gates.
Notes: This slide is animation based so view it in slide show mode for better understanding and colour of pairing in the k-map resembles the colour of corresponding term in the expression to avoid confusion.

## Slide 16: APPLICATIONS
Computers
Calculators
ATM
Mobile Phone
Integrated Circuits and so on......

## Slide 17: REFERENCES
http://only-vlsi.blogspot.com/2009/01/boolean-expression-simplification.html
https://www.google.com/search?tbm=isch&q=karnaugh+map+grouping&chips=q:karnaugh+map+grouping,g_1:k+map&usg=AI4_kQxn1GFLOgRA5XEOFWdHPcK4HmC8w&sa=X&ved=0ahUKEwie98rzl_3iAhWILo8KHcmABz0Q4lYIKygC&biw=1366&bih=657&dpr=1#imgrc=7j--zw4XwWyeiM:
Floyd & Jain, Digital Fundamentals, Pearson.
https://www.google.com/search?biw=1366&bih=657&tbm=isch&sa=1&ei=Ki4OXdSzG5L0rAH3jpjYCw&q=karnaugh+map+examples+with+solutions&oq=karnaugh+map+examples&gs_l=img.1.3.0j0i24l6.228061.233126..236212...0.0..1.463.4033.0j5j8j2j1......0....1..gws-wiz-img.......0i67j0i8i30.zfc8Yep3OZY#imgrc=nAjGgOZxU_LuCM:
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.
http://www.geeksforgeeks.org/digital-electronics-logic-design-tutorials/
http://www.ni.com/example/14493/en/
http://195.134.76.37/applets/AppletGates/Appl_Gates2.html

## Slide 18
THANK YOU