## Slide 1
DISCOVER . LEARN . EMPOWER
FULL ADDERS
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code 23ECH-101
Prepared By
Dr. Shikha
Unit-2 Chapter-1
Combinational and Sequential Circuits
Lecture No. 2.1.2

## Slide 2: Course Outcome
Figure 1.1 Practical application of Full Adder [4]
Full Adder
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 3: TYPES OF ADDERS
BINARY ADDER
HALF ADDER
FULL ADDER
PARALLEL ADDER
RIPPLE CARRY
LOOK AHEAD CARRY
CARRY SAVE
Figure 5 Types of Adders

## Slide 4: HALF ADDER
Half adder is a combinational logic circuit which add two input binary bits and will result sum and carry as output variables.
Figure 6 Block diagram of Half Adder

## Slide 5: HALF ADDER
Boolean Expression
S = A’B + AB’
S= A⊕B C=A.B
TRUTH TABLE
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Figure 7 Block diagram of Half Adder

## Slide 6: HALF ADDER
Figure 8 Logic diagram of Half Adder
Realization of the Boolean Expression

## Slide 7: FULL ADDER
Full adder is a combinational logic circuit which add two input binary bits and previous carry and will result sum and carry as output variables.
Figure 1 Block diagram of Full Adder

## Slide 8: FULL ADDER
A | B | Cin | S | c
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
TRUTH TABLE
Figure 2 Truth Table of Full Adder

## Slide 9: FULL ADDER
BOOLEAN EXPRESSION:
S=Á’B’ Cin+A’BCin’+AB’ Cin’+ABCin C=AB+BCin+CinA
Figure 3 Logic Diagram using basic gates

## Slide 10: FULL ADDER
Figure 4 Logic diagram of Full Adder
After Simplifying the Boolean Expression we obtain the following equation:
s= (A ⊕ B) ⊕ Cin
C=Cin(A ⊕ B)

## Slide 11: FULL ADDER
Figure 5 Logic diagram of FA using Half Adder

## Slide 12: Assessment Pattern
Design full adder using 2 half adders
Design full adder using gates
Design a full adder using only Basic Gates.

## Slide 13: APPLICATIONS
In ALU
Calculators
Delay Circuits

## Slide 14: REFERENCES
https://www.tutorialspoint.com/computer_logical_organization/combinational_circuits.htm
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.electronicshub.org%2Fhalf-adder-and-full-adder-circuits%2F&psig=AOvVaw3EEvl_U-utnhFfMkLwl-5x&ust=1595879743706000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCKja3bzZ6-oCFQAAAAAdAAAAABAP
https://www.google.com/url?sa=i&url=https%3A%2F%2Ftechyelf.blogspot.com%2F2017%2F09%2Fvhdl-code-for-full-adder-using-half.html&psig=AOvVaw2hfmDDKfQ5KlYO-MCeAhTk&ust=1595880483842000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCNi1lKTc6-oCFQAAAAAdAAAAABAa
https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.wired.com%2Fstory%2Fyou-can-power-a-calculator-with-some-leds%2F&psig=AOvVaw04qq4sVg6HobtSKaimt6_4&ust=1595881474357000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCNDS9f7f6-oCFQAAAAAdAAAAABAc
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.

## Slide 15
THANK YOU