## Slide 1
DISCOVER . LEARN . EMPOWER
De-Mux, Encoder & Decoder
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code 23ECH-101
Prepared By
Dr. Shikha
Unit-2 Chapter-2
DeMultiplexer
Lecture No. 2.1.5

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about the derivation of logic for the design of Demultiplexer.
2 | To aware about implementation of Demultiplexer circuit.
3 | To learn about design of different design of Demuktiplexer.

## Slide 3: Course Objectives
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4: Course Outcome
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create
DeMULTIPLEXER

## Slide 5: Contents
What is Demultiplexer.
Demux Types.
1-to-2 Line Demultiplexer.
1-to-4 Line Demultiplexer.
1-to-8 Line Demultiplexer.
1-to-8 Line Demultiplexer Truth Table.

## Slide 6: What is De-Multiplexer?
A DEMUX is a digital switch with a single input (source) and a multiple outputs (destinations).The select lines determine which output the input is connected to.
DEMUX TYPES
1-to-2 (1 select line)
1-to-4 (2 select lines)
1-to-8 (3 select lines)
1-to-16 (4 select lines)

## Slide 7: Functional Diagram Of a Demultiplexer
Fig 1: Functional Diagram Of a De-multiplexer

## Slide 8: Demultiplexer 1 to 2 line De-Multiplexer
Fig 2 1 to 2 line De-multiplexer

## Slide 9: 1- to- 4 line demultiplexer
Fig 3: 1 to 4 line De-multiplexer

## Slide 10: 1 : 8 Demultiplexer
Fig 4: 1 to 4 line De-multiplexer

## Slide 11: 1 : 8 Demultiplexer (Truth Table)
Fig 5: 1 to 4 line De-multiplexer

## Slide 12: De–Mux Tree

## Slide 14: ENCODER
An Encoder is a combinational logic circuit.
It performs the inverse operation of Decoder.
The opposite process of decoding is known as Encoding.
An Encoder converts an active input signal into a coded output signal.
Block diagram of Encoder is shown in Fig.1.1. It has ‘M’ inputs and ‘N’ outputs.
An Encoder has ‘M’ input lines, only one of which is activated at a given time, and produces an N-bit output code, depending on which input is activated.
- - - - - - -
- - - - - - -
‘M’
Inputs
‘N’ Outputs
Encoder
A0 A1
A2
AM-1
B0 B1
B2
BN-1
Fig. 6: - ENCODER DIAGRAM

## Slide 15
Encoders are used to translate the rotary or linear motion into a digital signal.
The difference between Decoder and Encoder is that Decoder has Binary Code as an input while Encoder has Binary Code as an output.
Encoder is an Electronics device that converts the analog signal to digital signal such as BCD Code.
Types of Encoders
Priority Encoder
Decimal to BCD Encoder
Octal to Binary Encoder
Hexadecimal to Binary Encoder

## Slide 16: ENCODER
Encoder 4 x 2
Decoder 2 x 4
A0 A1 A2
A3
M=4 M=22 M=2N
‘M’ is the input and ‘N’ is the output
B0
Fig. 7: ENCODER DIAGRAM
B
1
B2 B3

## Slide 17: ENCODER
Encoder 4 x 2
Decoder 2 x 4
A0 A1 A2 A3
M=4 M=22 M=2N
‘M’ is the input and ‘N’ is the output
00
01
10
11
Fig. 8 ENCODER DIAGRAM

## Slide 18: ENCODER
Encoder 4 x 2
A0 A
1
Decoder 2 x 4
A2 A3
M=4 M=22 M=2N
‘M’ is the input and ‘N’ is the output
00
01
10
11
1
0
Fig. 9: ENCODER DIAGRAM

## Slide 19: ENCODER
Encoder 4 x 2
A0 A
1
Decoder 2 x 4
A2 A3
M=4 M=22 M=2N
‘M’ is the input and ‘N’ is the output
00
01
10
11
1
0
10
Fig. 10: ENCODER DIAGRAM

## Slide 20: PRIORITY ENCODER
As the name indicates, the priority is given to inputs line.
If two or more input lines are high at the same time i.e 1 at the same time, then the input line with high priority shall be considered.
Block diagram and Truth table of Priority Encoder are shown in fig. 1.6.
D3
D2
D1
D0
Y1
Y0
Highest Priority
Input
Priority Encoder
INPUTS |  |  |  | OUTPUTS |  | V
D3 | D2 | D1 | D0 | Y1 | Y0 | 
0 | 0 | 0 | 0 | x | x | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | x | 0 | 1 | 1
0 | 1 | x | x | 1 | 0 | 1
1 | x | x | x | 1 | 1 | 1
TRUTH TABLE:
Fig. 1 1 : ENCODER DIAGRAM
Lowest Priority Output
Input
Block Diagram of Priority Encoder

## Slide 21
D3D2
D3D2
D1D0
D1D0
00 01 11 10
00 01 11 10
00
01
11
10
10
11
01
00
 | X | 0 | 1 | 1
 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
X |  | 0 | 0 | 0 | 
 | 1 | 1 | 1 | 1 | 
 | 1 | 1 | 1 | 1 | 
1 |  | 1 | 1 | 1 | 
2 1
3
0
Y  D  D D
Y1  D2  D3
There are four inputs D0, D1,D2, D3 and two outputs Y1 and Y2.
D3 has highest priority and D0 is at lowest priority.
If D3=1 irrespective of other inputs then output Y1Y0=11.
D3 is at highest priority so other inputs are considered as don’t care.
K-map for Y1 and Y0
Fig. 12 : ENCODER DIAGRAM

## Slide 22: LOGIC DIAGRAM OF PRIORITY ENCODER:
Y1  D2  D3
Y0  D2 D1 + D3
D3 D2 D1 D0
Y1
Y0
Fig. 13 : ENCODER DIAGRAM

## Slide 23: DECIMAL TO BCD ENCODER:
It has ten inputs corresponding to ten decimal digits (from 0 to 9) and four outputs (A,B,C,D) representing the BCD.
- - - - - - - - -
0
1
2
A
B
ENCODER
C
D
9
INPUTS
OUTPUTS
Fig. 14 : ENCODER DIAGRAM

## Slide 24: Truth Table
INPUTS |  |  |  |  |  |  |  |  |  | BCD OUTPUTS |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Fig. 15 : ENCODER DIAGRAM

## Slide 25
From Truth Table it is clear that the output A is HIGH when input is 8 OR 9 is HIGH
Therefore A=8+9
The output B is HIGH when 4 OR 5 OR 6 OR 7 is HIGH Therefore B=4+5+6+7
The output C is HIGH when 2 OR 3 OR 6 OR 7 is HIGH
Therefore C=2+3+6+7
Similarly D=1+3+5+7+9
Logic Diagram is shown in fig. 1.11

## Slide 26: DECIMAL TO BCD ENCODER
A
B
C
D
+5V
0
1
2
3
4
5
6
7
8
9
Fig. 16: ENCODER DIAGRAM

## Slide 27: OCTAL TO BINARY ENCODER
generates
Block Diagram of Octal to Binary Encoder is shown below.
It has eight inputs and three outputs.
Only one input has one value at any given time.
Each input corresponds to each octal digit and output
corresponding Binary Code.
D0 D1 D2 D3 D4 D5 D6 D7
X
Y
Z
INPUT
OUTPUT
ENCODER
Fig. 17: ENCODER DIAGRAM

## Slide 28: TRUTH TABLE
INPUT |  |  |  |  |  |  |  | OUTPUT |  | 
D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | X | Y | Z
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
Fig. 18 : ENCODER DIAGRAM

## Slide 29: X  D4  D5  D6  D7 Y  D2  D3  D6  D7 Z  D1  D3  D5  D7
D4 D5
D6
D7
X  D4  D5  D6  D7
Y  D2  D3  D6  D7
Z  D1  D3  D5  D7
Fig. 19: ENCODER DIAGRAM
LOGIC DIAGRAM
D0 D1 D2 D3

## Slide 30: Decoder

## Slide 31
Design of 2-to-4 Decoder

## Slide 33: Questions:
1. Implement the following function using 3:8 decoder.
Y0(A,B,C)=(0,1,2,4)
Y1(A,B,C)=(1,3,5,7)
Y2(A,B,C)=(4,5,6,7)
2. Design a full adder using 3 to 8 line decoder.

## Slide 34: REFERENCES
https://www.google.com/search?q=combinational+circuits+in+digital+electronics&source=lnms&tbm=isch&sa=X&ved=0ahUKEwj526-wnv3iAhWSXCsKHf77AtQQ_AUIESgC&biw=1366&bih=657#imgrc=v4c5n7-dy4fzAM:
https://www.tutorialspoint.com/computer_logical_organization/combinational_circuits.htm
https://www.google.com/search?biw=1366&bih=657&tbm=isch&sa=1&ei=eE8PXd3VHMn9vAS13YHoBA&q=multiplexer+circuit&oq=multiplexer+&gs_l=img.1.2.0i67j0l9.4913.5532..8609...0.0..0.400.1145.0j1j2j0j1......0....1..gws-wiz-img.......0i8i30j0i24.xyEOkXeoseI#imgrc=4KXE27M1oFg2EM:
https://www.google.com/search?biw=1366&bih=657&tbm=isch&sa=1&ei=iVMPXbH8KpWSwgPKnKBA&q=decoder+2%3A4&oq=decoder+2%3A4&gs_l=img.3...584113.590073..591350...0.0..0.1147.6168.2-3j0j1j3j1j2......0....1..gws-wiz-img.....0..0i67j0j0i30j0i5i30j0i8i30.SPtmY9c721k#imgrc=tVdWQmsIYObp-M:
https://www.google.com/search?biw=1366&bih=657&tbm=isch&sa=1&ei=e1oPXdL_HM2lwgPUqoTQAg&q=octal+encoder&oq=+octal+encoder&gs_l=img.1.4.0i7i30l4j0i24.1789.4192..7678...0.0..0.321.1624.0j1j5j1......0....1..gws-wiz-img.......0i67j0.VPdFtgfemxA#imgrc=IlDJe3yY21xN7M:
Floyd & Jain, Digital Fundamentals, Pearson.
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.

## Slide 35
THANK YOU