## Slide 1
DISCOVER . LEARN . EMPOWER
FLIP FLOPS
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code 23ECH-101
Prepared By
Dr. Shikha
Unit-2 Chapter-2
Combinational and Sequential Circuits
Lecture No. 2.1.7

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about the derivation of logic for the design of Sequential Circuits.
2 | To aware about implementation of Sequential Circuits.
3 | To learn about design of different design of Sequential Circuits.

## Slide 3: Course Objectives
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4
SEQUENTIAL CIRCUITS
Course Outcome
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 5: SEQUENTIAL CIRCUITS
  Introduction to Sequential Circuit
  Difference between Latch & Flip Flop
  Types of Flip Flops
  SR Flip Flop in details
Figure 2: Sequential circuit

## Slide 6: INTRODUCTION TO SEQUENTIAL CIRCUIT
Sequential circuit provides an output based on current input and past input variables [3].
Sequential circuits consists of memory elements to store binary information.
Figure 3 Basic of the Sequential circuit

## Slide 7: CLASSIFICATION OF SEQUENTIAL CIRCUITS
Event Driven
Clock Driven
Pulse Driven
Figure 3 Classification of Sequential circuit

## Slide 8: SEQUENTIAL FEEDBACK LOOP
To retain their current state, sequential circuits rely on feedback.
In feedback a fraction of the output is fed back to the input.
Figure 4 Feedback in Sequential circuit

## Slide 9: LATCH
Latches are basic storage elements which operate with signal levels.
Latches controlled by a clock transition are known as flip-flops.
These are level-sensitive devices.
Latches are used for the design of the asynchronous sequential circuit.
Flip Flop are made from Latches.

## Slide 10: WORKING OF LATCH
SR Latch
Figure 5: SR Latch

## Slide 11: DIFFERENCE BETWEEN LATCH AND FLIP FLOP
Latch | Flip Flop
It does not require clock signal. | It requires clock signal.
It is level sensitive device. | It is edge sensitive.
Power requirement is less. | Power requirement is more.
Fast operation. | Slow operation.

## Slide 12: FLIP FLOP
Flip-flop is a basic digital memory circuit, which stores one bit of information.
Flip flops are the fundamental blocks of most sequential circuits.
It is also known as a bistable multivibrator or a binary or one-bit memory.
Flip-flops are used as memory elements in sequential circuit.
Clocked flip flops serve as memory elements in synchronous sequential circuits.
Unclocked flip-flops (i.e., latches) serve as memory elements in asynchronous sequential circuits.

## Slide 13: TYPES OF FLIP FLOPS
Figure 6: Types of Flip Flops

## Slide 14: Symbols of Flip Flops
Figure 7 Symbols of Flip Flops

## Slide 15: 1-bit Memory Cell Using NAND Gate
S | R | Q | Q’ | 
0 | 0 | Race | Race | 
0 | 1 | 0 | 1 | Reset
1 | 0 | 1 | 0 | Set
1 | 1 | Same as previous | Same as previous | 

## Slide 16: 1-bit Memory Cell Using NOR Gate
S | R | Q | Q’ | 
0 | 0 | Same as previous | Same as previous | 
0 | 1 | 0 | 1 | Reset
1 | 0 | 1 | 0 | Set
1 | 1 | Race | Race | 

## Slide 17: SR FLIP FLOP
It is also known as SR Latch.
It is a sequential circuit.
It is one-bit memory bistable device.
It has two outputs:
  “SET” the device (output = “1”).
  “RESET” the device (output = “0”).
Figure 8 SR Flip Flop Symbol Diagram

## Slide 19: SR FLIP FLOP WORKING
Figure 9 SR Flip Flop Logic Diagram
Figure 10: SR Flip Flop Truth Table

## Slide 20: Cont…
Figure 11: SR Flip Flop Switching Diagram

## Slide 21: NAND GATE SR FLIP FLOP
Figure 12 NAND Gate SR Flip Flop

## Slide 22: NOR GATE SR FLIP FLOP
Figure 13 NOR Gate SR Flip Flop

## Slide 24: ADVANTAGES AND DISADVANTAGES
Advantages
  Useful in building synchronously clocked logic.
Disadvantages
  The SR Flip flop is not edge triggerable. Most Flip Flop circuits require edge triggering.
  There is a more complex Flip Flop designed.
  by Jack King that is very
  The limits of the SR Flip Flop are overcome by cascading a second stage in the circuit which is arranged with a clock /clock line to cause an edge triggering option. The most basic version is called a D Flip Flop wherein D stands for Data.

## Slide 25: APPLICATIONS
Registers
RAM (Random Access Memory)
Counters
Frequency Divider circuits
Data transfer
Static RAM
Microprocessor registers & latches
Shift registers
Counters
Switch debouncing
Oscillators
Signal conditioning and synchronization

## Slide 26: ASSESSMENT PATTERN
Explain SR flip-flop.
Explain NAND gate S-R flip-flop.
For the clocked SR flip-flop writ the state table, draw the state diagram and the state equation.
For the clocked SR flip-flop writ the state table, draw the state diagram and the state equation.
Explain triggering of flip-flops with waveform.

## Slide 27: REFERENCES
https://www.google.com/search?q=flip+flops+in+digital+electronics&source=lnms&tbm=isch&sa=X&ved=0ahUKEwjv46Hyu__iAhWMuY8KHVMCAxoQ_AUIESgC&biw=1366&bih=657#imgrc=Jr0JsbzuxbBXUM:
https://www.electronics-tutorials.ws/sequential/seq_1.html
https://www.geeksforgeeks.org/introduction-of-sequential-circuits/#:~:text=Combinational%20circuit%20produces%20an%20output,capable%20of%20storing%20binary%20information.
https://www.electronicshub.org/flip-flops/
https://www.allaboutcircuits.com/textbook/digital/chpt-10/s-r-latch/
https://www.electronicshub.org/jk-flipflop/
https://www.electrical4u.com/master-slave-flip-flop/
https://www.gatevidyalay.com/flip-flops-in-electronics/
https://www.electricaltechnology.org/2019/09/digital-flip-flop-and-latches-symbols.html
http://hades.mech.northwestern.edu/index.php/Flip-Flops_and_Latches
https://www.electronicshub.org/t-flip-flop/
https://www.electronics-tutorial.net/sequential-logic-circuits/toggle-flip-flop/
https://www.electronicshub.org/flip-flop-applications/
https://www.quora.com/What-is-the-function-of-flip-flops
Floyd & Jain, Digital Fundamentals, Pearson.
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.

## Slide 28
THANK YOU