## Slide 1
DISCOVER . LEARN . EMPOWER
J-K & T Flip Flop
INSTITUTE UIE
DEPARTMENT ACADEMIC UNIT-1
Bachelor of Engineering (Computer Science & Engineering)
Subject Name Introduction Electrical & Electronics Engineering
Subject Code 23ECH-101
Prepared By
Dr. Shikha
Unit-2 Chapter-2
Combinational and Sequential Circuits
Lecture No. 2.1.8

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about the derivation of logic for the design of Sequential Circuits.
2 | To aware about implementation of Sequential Circuits.
3 | To learn about design of different design of Sequential Circuits.

## Slide 3: Course Objectives
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4
SEQUENTIAL CIRCUITS
Course Outcome
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 5: SEQUENTIAL CIRCUITS
  JK Flip Flop in detail
  T Flip Flop in detail

## Slide 6: JK FLIP FLOP
The basic S-R flip-flop suffers from two basic switching problems.
  S = R = 0, must always be avoided.
  If Set or Reset change state while the enable (EN) input is high the correct latching action may not occur.
To overcome these two fundamental design problems with the SR flip-flop design, the JK flip Flop was developed.
The difference this time is that the “JK flip flop” has no invalid or forbidden input states of the SR Latch.
The JK flip flop is basically a gated SR flip-flop with the addition of a clock input circuitry that prevents the illegal or invalid output condition.

## Slide 7: JK FLIP FLOP WORKING
Figure 1 JK Flip Flop Logic Diagram

## Slide 8
Figure 2 JK Flip Flop Truth Table

## Slide 9: Cont…
Figure 3 JK Flip Flop Switching Diagram

## Slide 10: NAND GATE JK FLIP FLOP
Figure 4 JK Flip Flop NAND gate Diagram
Figure 5 JK Flip Flop NAND gate Truth Table

## Slide 11: ADVANTAGES AND DISADVANTAGES
Advantages
  There is no invalid states and the JK flip-flop can operate as a set/reset flip-flop.
  When the two inputs are tied together, the JK flip-flop can act as a T flip-flop that is widely used in binary counters.
Disadvantages
  When both the inputs and clock pulse signal are at level 1 after the output is complemented once, output transmission will start getting repeated and continuous. This results in a raised condition.

## Slide 12: T FLIP FLOP
T flip – flop is also known as “Toggle Flip – flop”.
To avoid the occurrence of intermediate state in SR flip – flop, we should provide only one input to the flip – flop called Trigger input or Toggle input (T).
Then the flip – flop acts as a Toggle switch.
Toggling means ‘Changing the next state output to complement of the present state output’.

## Slide 13: T FLIP FLOP WORKING
Figure 6 T Flip Flop Logic Diagram
Figure 7 T Flip Flop Truth Table

## Slide 14: Cont…
Figure 8 T Flip Flop Logic Diagram

## Slide 15: ADVANTAGES AND DISADVANTAGES
Advantages
  These Flip-Flops has a toggle input and a clock. When a clock is triggered it inverts the value of Flip-Flops.
  They are good for counters.
Disadvantages
  The state of Flip-Flop is known only when the previous state is known.
  They are not available as IC’s, hence they are constructed using JK Flip-Flop, D Flip-Flop etc.

## Slide 16: ASSESSMENT PATTERN
Explain JK flip-flop.
Explain NAND gate JK flip-flop.
For the clocked JK flip-flop write the state table, draw the state diagram and the state equation.
For the clocked T flip-flop writ the state table, draw the state diagram and the state equation.
Explain triggering of flip-flops with waveform.

## Slide 17: APPLICATIONS
Registers
RAM (Random Access Memory)
Counters
Frequency Divider circuits
Data transfer [13]
Static RAM
Microprocessor registers & latches
Shift registers
Counters
Switch debouncing
Oscillators
Signal conditioning and synchronization

## Slide 18: REFERENCES
https://www.google.com/search?q=flip+flops+in+digital+electronics&source=lnms&tbm=isch&sa=X&ved=0ahUKEwjv46Hyu__iAhWMuY8KHVMCAxoQ_AUIESgC&biw=1366&bih=657#imgrc=Jr0JsbzuxbBXUM:
https://www.electronics-tutorials.ws/sequential/seq_1.html
https://www.geeksforgeeks.org/introduction-of-sequential-circuits/#:~:text=Combinational%20circuit%20produces%20an%20output,capable%20of%20storing%20binary%20information.
https://www.electronicshub.org/flip-flops/
https://www.allaboutcircuits.com/textbook/digital/chpt-10/s-r-latch/
https://www.electronicshub.org/jk-flipflop/
https://www.electrical4u.com/master-slave-flip-flop/
https://www.gatevidyalay.com/flip-flops-in-electronics/
https://www.electricaltechnology.org/2019/09/digital-flip-flop-and-latches-symbols.html
http://hades.mech.northwestern.edu/index.php/Flip-Flops_and_Latches
https://www.electronicshub.org/t-flip-flop/
https://www.electronics-tutorial.net/sequential-logic-circuits/toggle-flip-flop/
https://www.electronicshub.org/flip-flop-applications/
https://www.quora.com/What-is-the-function-of-flip-flops
Floyd & Jain, Digital Fundamentals, Pearson.
Mano,Morris, Digital Design, Prentice Hall of India.
Fletcher, An Engg. Approach to digital design, Prentice Hall of India.

## Slide 19
THANK YOU