## Slide 1
DISCOVER . LEARN . EMPOWER
UNIVERSITY INSTITUTE OF ENGINEERING
DEPARTMENT OF ACADEMIC UNIT-1
Bachelor of Engineering (CSE)
SUBJECT NAME: Introduction to Electrical & Electronics Engineering-IEEE
SUBJECT CODE : 23ECH-101
By
Dr. Shikha
Unit-3 Chapter-1
INTRODUCTION TO TRANSFORMER
Lecture No.3.1.1

## Slide 2: Lecture Objectives
S. No. | Objectives
1 | To make student aware about faraday’s law of electromagnetic induction
2 | To aware about introduction to transformer and its working principle
3 | To provide knowledge about different types of transformer
4 | To aware about construction of core type and shell type transformer
5 | To give knowledge about transformation ratio of transformer
https://www.quora.com/What-are-the-differences-between-a-circuit-and-an-electric-circuit

## Slide 3: Course Objectives
https://www.quora.com/What-are-the-differences-between-a-circuit-and-an-electric-circuit
S. No. | Objectives
1 | Understand Electrical & Electronics Engineering Fundamentals
2 | To prepare students to perform the analysis and design of various Electrical & digital electronic circuits.

## Slide 4: Course Outcomes
https://in.pinterest.com/pin/240661173823316229/
CO Number | Title | Level
CO1 | To identify the different types of electrical elements and the basic op-amp circuit elements and to illustrate the various types of motors, transducers. | Remember
CO2 | To understand basic principles of transformers, transducers, op-amps, DC and AC motors and to compare the different methods for analysing electrical and magnetic circuits. | Understand
CO3 | To derive the relationships between parameters in electric and magnetic circuits and motors and to determine specifications of op-amps. | Analyze
CO4 | To solve the basic problems related to electric circuits, magnetic circuits and motors and to assess the characteristics of different configurations of op-amps. | Evaluate
CO5 | To design the different applications of transducers, motors as well as the op-amps like adders, subtractor and comparators. | Create

## Slide 5: Importance of Introduction of Electrical & Electronics Engineering
Use from home appliances to industrial plants.
Usage in communication and satellite navigation system.
Handles in electronics equipment and computers.
Deals with the problem of power transmission and motor control.
Control and monitor the medical appliances in hospitals.
High voltage applications with heavy current.
Robotics applications.
Product designing and development.

## Slide 6: Contents
Faraday’s Law of Electromagnetic Induction
Types of induced emf
Self induced emf
Mutual induced emf
Introduction of single phase transformer
Working Principle of Single Phase Transformer
Different types of transformer
Step up transformer
Step down transformer
Construction of Transformer
core type
shell type
Transformation ratio
Notes: Computer in the diagram is 3rd generation computer. The period of third generation was from 1965-1971. The computers of third generation used Integrated Circuits (ICs) in place of transistors. A single IC has many transistors, resistors, and capacitors along with the associated circuitry. The main features of third generation are −
IC used
More reliable in comparison to previous two generations
Smaller size
Generated less heat
Faster
Lesser maintenance
Costly
AC required
Consumed lesser electricity
Supported high-level language

## Slide 7: Faraday’s Law of Electromagnetic Induction
Faraday’s 1st law: Whenever a conductor is placed in a varying magnetic field, an electromotive force is induced. If the conductor circuit is closed, a current is induced which is called induced current.
Here are a few ways to change the magnetic field intensity in a closed loop:
By rotating the coil relative to the magnet.
By moving the coil into or out of the magnetic field.
By changing the area of a coil placed in the magnetic field.
https://www.electrical4u.net/wp-content/uploads/2018/06/Faradays-Law-of-electronagnetic-indution-6.png
Fig-1 Electromagnetic induction

## Slide 8: Faraday’s Law of Electromagnetic Induction
Faraday’s 2nd Law:The induced emf in a coil is equal to the rate of change of flux linkage.
The flux is the product of the number of turns in the coil and the flux associated with the coil. The formula of Faraday’s law is given below:
Therefore,
E=Ndϕ/dt
Considering Lenz’s law,
E=−Ndϕ/dt
https://www.electrical4u.net/wp-content/uploads/2018/06/Faradays-Law-of-electronagnetic-indution-6.png
Fig-2 Electromagnetic induction
Notes: Same as fig -3

## Slide 9: Classification of Induced EMF
https://circuitglobe.com/wp-content/uploads/2015/08/indufced-emf.jpg
Table-1 Classification of induced EMF
Notes: Fig-5

## Slide 10: Self Induced EMF
Consider a coil having N number of turns as shown in the figure. When the switch S is closed & current I flows through the coil, it produces flux (φ) linking with its own turns.
If the current flowing through the coil is changed by changing the value of resistance (R), the flux linking with it, changes and hence emf is induced in the coil.

## Slide 11: Self Induced EMF
This induced emf is called Self Induced emf. The direction of this induced emf opposes the change of current in the coil. This effect is because of Lenz’s Law.
The magnitude of self-induced emf is directly proportional to the rate of change of current in the coil. L is constant of proportionality and called as Self Inductance.
https://images.app.goo.gl/zREgsGt6emmhV83GA
Fig-3 Self induced EMF

## Slide 12: Mutual Induced EMF
The emf induced in a coil due to the change of flux produced by another neighbouring coil linking to it, is called Mutually Induced emf.
When the switch (S) is closed in the circuit shown above, current I1 flows through the coil A, and it produces the fluxφ1. Most of the flux says φ12 links with the other coil B.
https://www.quora.com/What-is-the-difference-between-a-self-induced-EMF-and-a-mutually-induced-EMF
Fig-4 Mutually induced EMF

## Slide 13: Mutual Induced EMF
If the current flowing through the coil A is changed by changing the value of variable resistor R, it changes flux linking with the other coil B and hence emf is induced in the coil.
This induced emf is called Mutually Induced emf.
https://www.quora.com/What-is-the-difference-between-a-self-induced-EMF-and-a-mutually-induced-EMF
Same as Fig-4 Mutually induced EMF

## Slide 14: Single Phase Transformer
The transformer is the static device which works on the principle of electromagnetic induction.
It is used for transferring the electrical power from one circuit to another without any variation in their frequency.
In electromagnetic induction, the transfer of energy from one circuit to another takes places by the help of the mutual induction. i.e the flux induced in the primary winding is linked with the secondary winding.

## Slide 15
Working principle of electrical power transformer is similar to that of mutual induction.
A transformer is a static (or stationary) piece of apparatus by means of which electric power in one circuit is transformed into electric power of the same frequency in another circuit.
It can raise or lower the voltage in a circuit but with a corresponding decrease or increase in current.
Working Principle of Single Phase Transformer
https://images.app.goo.gl/7ybQWzfTwcuKTP4PA
Fig-5 Single phase Transformer

## Slide 16
The physical basis of a power transformer is mutual induction between two circuits linked by a common magnetic flux.
In its simplest form, it consists of two inductive coils which are electrically separated but magnetically linked through a path of low reluctance.
Working Principle of Single Phase Transformer
https://images.app.goo.gl/7ybQWzfTwcuKTP4PA
Same as Fig-5 Single phase Transformer

## Slide 17
The two coils possess high mutual inductance. If one coil is connected to a source of alternating voltage, an alternating flux is set up in the laminated core, most of which is linked with the other coil in which it produces mutually-induced e.m.f. (according to Faraday’s Law of Electromagnetic Induction e = M.dI/dt).
If the second coil circuit is closed, a current flow in it and so electric energy is transferred (entirely magnetically) from the first coil to the second coil.
The first coil, in which electric energy is fed from the a.c. supply mains is called primary winding and the other from which energy is drawn out, is called secondary winding.
Working Principle of Single Phase Transformer

## Slide 18
There are two types of a transformer
Step –up
Step-down
Different types of a transformer

## Slide 19
A transformer in which the output (secondary) voltage is greater than its input (primary) voltage is called a step-up transformer.
The E1 and E2 are the voltages, and T1 and T2 are the number of turns on the primary and secondary winding of the transformer
The number of turns on the secondary of the transformer is greater than that of the primary, i.e., T2 > T1.
Step-up Transformer
https://circuitglobe.com/wp-content/uploads/2016/11/step-down-transformer.jpg
Fig-6 Step up transformer

## Slide 20
A transformer in which the output (secondary) voltage is less than its input (primary) voltage is called a step-down transformer.
The number of turns on the primary of the transformer is greater than the turn on the secondary of the transformer, i.e., T2 < T1. The step-down transformer is shown in the figure below.
The voltage turn ratio of the step-down transformer is 2:1.
Step down transformer
https://circuitglobe.com/wp-content/uploads/2016/11/step-up-transformer.jpg
Fig-7 Step down Transformer

## Slide 21: Construction of Transformer
The transformers are of two general types, distinguished from each other merely by the manner in which the primary and secondary coils are placed around the laminated core.
The two types are known as
(i) core-type transformer (ii) shell-type transformer

## Slide 22
Core Type Transformer
The magnetic core of the transformer is made up of laminations to form a rectangular frame. The laminations are cut in the form of L-shape strips shown in the figure below.
For avoiding the high reluctance at the joints where laminations are butted against each other, the alternate layer is stacked differently to eliminate continues joints.
Fig-8 core type Core
https://circuitglobe.com/wp-content/uploads/2017/01/shell-type-transformer-circuit.jpg

## Slide 23
Core type transformer
The primary and secondary windings are interleaved to reduce the leakage flux.
Half of each winding is placed side by side or concentrically on the leg of the core as shown in the figure below.
For simplicity, the primary and secondary winding is located on the separate limbs of the core.
https://circuitglobe.com/wp-content/uploads/2017/01/shell-type-transformer-circuit.jpg
Fig-9 Core type Transformer

## Slide 24
Shell Type Transformer
The laminations are cut in the form of a long strip of E’s, and I’s as shown in the figure.
To reduce the high reluctance at the joints where the lamination are butted against each other, the alternate layers are stacked differently to eliminate continuous joint.
The shell type transformer has three limbs or legs. The central limb carries the whole of the flux, and the side limb carries the half of the flux. Hence the width of the central limb is about to double to that of the outer limbs.
https://circuitglobe.com/wp-content/uploads/2017/01/shell-type-transformer-circuit.jpg
Fig-10 Shell type Core

## Slide 25
Shell Type Transformer
The primary and secondary both the windings are placed on the central limbs.
The low voltage winding is placed near the core, and the high voltage winding is placed outside the low voltage winding to reducing the cost of insulation placed between the core and the low voltage winding.
The windings are cylindrical, and the core laminations are inserted on it.
https://circuitglobe.com/wp-content/uploads/2017/01/shell-type-transformer-circuit.jpg
Fig-11 Shell Type Transformer

## Slide 26: Transformation Ratio
The transformer transformation ratio or transformer turns ratio (K) is the quotient value obtained by dividing the number of turns of the primary winding (N1) and the number of turns of the secondary winding (N2).
Then
K = N1/N2
Further we may write
K = N1/N2 = V1/V2 = I2/I1

## Slide 27
To step-down long-distance signals to support both residential and light-
commercial electronic devices.
In television sets for voltage regulation.
To step-up power in home inverters.
To supply power to non-urban areas.
To isolate two circuits electrically as primary and secondary are placed far
from each other.
The applications of a single-phase transformer are mentioned below.
Applications of Single-phase transformer

## Slide 28: Frequently Asked Questions
1.) What does a single-phase mean?
Answer:- A single-phase system or circuit which generates or uses single alternating voltage.
2.) Do houses use single-phase supply?
Answer:- Generally, homes are supplied with single-phase supply.
3.) On which principles does the single-phase transformer operate?
Answer:- Faraday’s law of Electromagnetic Induction and Mutual Induction.

## Slide 29: Frequently Asked Questions
4.) What is the transformer “Turns Ratio”?
Answer:- N1/N2 = V1/V2 = K = Turns Ratio
5.) Give two uses of a single-phase transformer
Answer:-
In television sets for voltage regulation
To step-up power in home inverters

## Slide 30: Summary
Through this PPT , the students have learned and understood
Terminology of magnetic circuits.
Concept of self and mutual induction.
Principle of operation of transformers.
Construction of transformers
Performance analysis of transformers

## Slide 31: Learning Outcomes
To make students understand the
Terminology of magnetic circuits.
Concept of self and mutual induction.
Principle of operation of transformers.
Construction of transformers
Performance analysis of transformer
https://www.google.com/search?q=transformer+working+and+construction&source=lnms&tbm=isch&sa=X&ved=2ahUKEwjf7q2zo5XqAhXbb30KHcZ1A-MQ_AUoAnoECBEQBA&biw=1366&bih=608#imgrc=Hz4hgKww9splRM&imgdii=-GHifX4ZDm1raM
Fig-16

## Slide 32: Course Outcome to Program Outcome Relationship
 |  | (20ELT-111) BEEE |  |  |  |  |  |  |  |  |  | 
PO→ |  |  |  |  |  |  |  |  |  |  |  | 
CO↓ | PO1 | PO2 | PO3 | PO4 | PO5 | PO6 | PO7 | PO8 | PO9 | PO10 | PO11 | PO12
CO1 | 3 | 3 | 2 | 2 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
CO2 | 3 | 0 | 2 | 0 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 0
CO3 | 3 | 1 | 1 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 1 | 0
CO4 | 3 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 33: Assessment Pattern
A Assignment (each assignment) | B Time Bound Surprise Test (each test) | C Quiz (each quiz) | D Mid Semester Test(one per test) | E Homework | F Discussion Forums | G Attendance and engagement Score on BB
10 | 12 | 4 | 20 | NA | NA | 2

## Slide 34: References
https://iopscience.iop.org/book/978-0-7503-2084-9/chapter/bk978-0-7503-2084-9ch1
https://circuitglobe.com/what-is-a-transformer.html
https://cnx.org/contents/FOAgj46E@1.1:CF55C3SF@1/chapter-1-Magnetic-Circuits-and-Magnetic-Materials
https://www.electronics-tutorials.ws/transformer/transformer-basics.html

## Slide 35
THANK YOU
For queries
Email:kanchanbharti.ee@cumail.in