## Slide 1
University Institute of Engineering
Department of Computer Science & Engineering
COMPUTER ORGANIZATION & ARCHITECTURE
(23CST-204/23ITT-204)
ER. SHIKHA ATWAL
E11186
ASSISTANT PROFESSOR
BE-CSE

## Slide 2
Operations In The Instruction Set
Instruction Set is a collection of instructions that a CPU can execute. These instructions are categorized based on the type of operation they perform.
Here's a breakdown of the operations commonly found in an instruction set:
1. Arithmetic and Logical Operations: This category of instructions including Arithmetic Operations perform mathematical computations such as addition, subtraction, multiplication, and division.
Examples of Arithmetic Instructions:

## Slide 3
Instruction | Description | Example
ADD R1, R2 | Adds the contents of R2 to R1. | ADD AX, BX (x86).
SUB R1, R2 | Subtracts the contents of R2 from R1. | SUB AX, BX (x86).
MUL R1, R2 | Multiplies the contents of R1 and R2. | MUL BX (x86).
DIV R1, R2 | Divides R1 by R2. | DIV BX (x86).
INC R1 | Increments the value of R1 by 1. | INC AX (x86).
DEC R1 | Decrements the value of R1 by 1. | DEC CX (x86).
NEG R1 | Negates the value in R1. | NEG AX (x86).
ADC R1, R2 | Adds R2 to R1 with carry. | ADC AX, BX (x86).
SBB R1, R2 | Subtracts R2 from R1 with borrow. | SBB AX, BX (x86).

## Slide 4
These instructions perform bitwise logical manipulations, such as AND, OR, XOR, NOT, and shifts.
Examples of Logical Instructions:
Instruction | Description | Example
AND R1, R2 | Performs bitwise AND of R1 and R2. | AND AX, BX (x86).
OR R1, R2 | Performs bitwise OR of R1 and R2. | OR AX, BX (x86).
XOR R1, R2 | Performs bitwise XOR of R1 and R2. | XOR AX, BX (x86).
NOT R1 | Complements the bits of R1. | NOT AX (x86).
SHL R1, n | Shifts bits of R1 to the left by n positions. | SHL AX, 1 (x86).
SHR R1, n | Shifts bits of R1 to the right by n positions. | SHR AX, 1 (x86).
ROL R1, n | Rotates bits of R1 to the left by n positions. | ROL AX, 1 (x86).

## Slide 5
Instruction | Description | Example
ROR R1, n | Rotates bits of R1 to the right by n positions. | ROR AX, 1 (x86).
TEST R1, R2 | Performs bitwise AND without affecting registers, sets flags. | TEST AX, BX (x86).
At the end of execution of arithmetic and logical instructions, depending on the result in Accumulator, Condition Codes (Zero, Sign, Overflow, carry – ZSOC) are set, implying the outcome of the instruction execution. Generally, these flags are useful in controlling the flow of the program.

## Slide 6
2. Data Transfer Operations: These types of instructions move data between registers, memory, and I/O devices.
Examples of Data Transfer Instructions:
Instruction | Description | Example
MOV R1, R2 | Moves data from R2 to R1. | MOV AX, BX (x86).
LD R1, ADDR | Loads data from memory address into R1. | LDA 2000H (8085).
ST R1, ADDR | Stores the contents of R1 into memory address. | STA 3000H (8085).
PUSH R1 | Pushes the contents of R1 onto the stack. | PUSH AX (x86).
POP R1 | Pops the top value from the stack into R1. | POP AX (x86).
IN R1, PORT | Inputs data from an I/O port into R1. | IN AX, 60H (x86).
OUT PORT, R1 | Outputs data from R1 to an I/O port. | OUT 60H, AX (x86).
LEA R1, ADDR | Loads the address of memory into R1. | LEA AX, [BX+SI] (x86).
XCHG R1, R2 | Exchanges the contents of R1 and R2. | XCHG AX, BX (x86).

## Slide 7
3. Timing and Control Operations: These instructions are used to manage program flow, control system hardware, and manage the processor state.
Examples of Timing and Control Instructions:
Instruction | Description | Example
NOP | No operation; used for timing or delays. | NOP (x86,8085).
HLT | Halts the processor until a reset signal is received. | HLT (8085).
WAIT | Waits for an external signal to continue execution. | WAIT (x86).
CLC | Clears the carry flag. | CLC (x86).
STC | Sets the carry flag. | STC (x86).

## Slide 8
Instruction | Description | Example
CLI | Clears the interrupt flag (disables interrupts). | CLI (x86).
STI | Sets the interrupt flag (enables interrupts). | STI (x86).
INT n | Generates a software interrupt. | INT 21H (x86).
RET | Returns from a subroutine or interrupt handler. | RET (x86).
JMP ADDR | Jumps to the specified address unconditionally. | JMP 2000H (8085).
CALL ADDR | Calls a subroutine at the specified address. | CALL 3000H (8085).
RST n | Resets the processor and jumps to a fixed address. | RST 7 (8085).

## Slide 9
References
Reference Books:
J.P. Hayes, “Computer Architecture and Organization”, Third Edition.
Mano, M., “Computer System Architecture”, Third Edition, Prentice Hall.
Stallings, W., “Computer Organization and Architecture”, Eighth Edition, Pearson Education.
Text Books:
Carpinelli J.D,” Computer systems organization &Architecture”, Fourth Edition, Addison Wesley.
Patterson and Hennessy, “Computer Architecture” , Fifth Edition Morgaon Kauffman.

## Slide 10
Reference Website
Instruction Set Architecture : Instructions and Formats | Computer Architecture (witscad.com)
Computer Organization | Instruction Formats (Zero, One, Two and Three Address Instruction) - GeeksforGeeks
Computer Organization AND Security - COMPUTER ORGANIZATION AND SECURITY Computer Organization: - Studocu