## Slide 1
University Institute of Engineering
Department of Computer Science & Engineering
COMPUTER ORGANIZATION & ARCHITECTURE
(23CST-204/23ITT-204)
ER. SHIKHA ATWAL
E11186
ASSISTANT PROFESSOR
BE-CSE

## Slide 2
PERFORMANCE OF A PIPELINED PROCESSOR
Consider a ‘k’ segment pipeline with clock cycle time as ‘Tp’. Let there be ‘n’ tasks to be completed in the pipelined processor. Now, the first instruction is going to take ‘k’ cycles to come out of the pipeline but the other ‘n – 1’ instructions will take only ‘1’ cycle each, i.e, a total of ‘n – 1’ cycles. So, time taken to execute ‘n’ instructions in a pipelined processor:
ETpipeline = k + n – 1 cycles
= (k + n – 1) Tp
In the same case, for a non-pipelined processor, execution time of ‘n’ instructions will be: ETnon-pipeline = n * k * Tp

## Slide 3
So, speedup (S) of the pipelined processor over non-pipelined processor, when ‘n’ tasks are executed on the same processor is:
S = Performance of pipelined processor /Performance of Non-pipelined processor
As the performance of a processor is inversely proportional to the execution time, we have, S = ETnon-pipeline / ETpipeline
=> S = [n * k * Tp] / [(k + n – 1) * Tp] S = [n * k] / [k + n – 1]
When the number of tasks ‘n’ are significantly larger than k, that is, n >> k S = n * k / n
S = k
where ‘k’ is the number of stages in the pipeline.

## Slide 4
Also, Efficiency = Given speed up / Max speed up = S / Smax We know that, Smax = k
So, Efficiency = S / k
Throughput = Number of instructions / Total time to complete the instructions So, Throughput = n / (k + n – 1) * Tp
Note: The cycles per instruction (CPI) value of an ideal pipelined processor is 1

## Slide 5
Simple example
Consider a nonpipelined machine with 6 execution stages of lengths 50 ns, 50 ns, 60 ns, 60 ns, 50 ns, and 50 ns.
- Find the instruction latency on this machine.
- How much time does it take to execute 100 instructions?
Solution:
Instruction latency = 50+50+60+60+50+50= 320 ns
Time to execute 100 instructions = 100*320 = 32000 ns

## Slide 6
Suppose we introduce pipelining on this machine. Assume that when introducing pipelining, the clock skew adds 5ns of overhead to each execution stage.
What is the instruction latency on the pipelined machine?
How much time does it take to execute 100 instructions?
Solution:
Remember that in the pipelined implementation, the length of the pipe stages must all be the same, i.e., the speed of the slowest stage plus overhead. With 5ns overhead it comes to:
The length of pipelined stage = MAX(lengths of unpipelined stages) + overhead = 60 + 5 = 65 ns
Instruction latency = 65 ns
Time to execute 100 instructions = 65*6*1 + 65*1*99 = 390 + 6435 = 6825 ns

## Slide 7
What is the speedup obtained from pipelining?
Solution:
Speedup is the ratio of the average instruction time without pipelining to the average instruction time with pipelining.
(here we do not consider any stalls introduced by different types of hazards which we will look at in the next section)
Average instruction time not pipelined = 320 ns Average instruction time pipelined = 65 ns Speedup for 100 instructions = 32000 / 6825 = 4.69

## Slide 8
Problem-01:
Consider a pipeline having 4 phases with duration 60, 50, 90 and 80 ns. Given latch delay is 10 ns. Calculate-
  Pipeline cycle time
  Non-pipeline execution time
  Speed up ratio
  Pipeline time for 1000 tasks
  Sequential time for 1000 tasks
  Throughput

## Slide 9
Solution-
Given-
Four stage pipeline is used
Delay of stages = 60, 50, 90 and 80 ns
Latch delay or delay due to each register = 10 ns
Part-01: Pipeline Cycle Time-
Cycle time
= Maximum delay due to any stage + Delay due to its register
= Max { 60, 50, 90, 80 } + 10 ns
= 90 ns + 10 ns
= 100 ns

## Slide 10
Part-02: Non-Pipeline Execution Time-
Non-pipeline execution time for one instruction
= 60 ns + 50 ns + 90 ns + 80 ns
= 280 ns
Part-03: Speed Up Ratio-
Speed up
= Non-pipeline execution time / Pipeline execution time
= 280 ns / Cycle time
= 280 ns / 100 ns
= 2.8

## Slide 11
Part-04: Pipeline Time For 1000 Tasks-
Pipeline time for 1000 tasks
= Time taken for 1st task + Time taken for remaining 999 tasks
= 1 x 4 clock cycles + 999 x 1 clock cycle
= 4 x cycle time + 999 x cycle time
= 4 x 100 ns + 999 x 100 ns
= 400 ns + 99900 ns
= 100300 ns
Part-05: Sequential Time For 1000 Tasks-
Non-pipeline time for 1000 tasks
= 1000 x Time taken for one task
= 1000 x 280 ns
= 280000 ns

## Slide 12
Part-06: Throughput-
Throughput for pipelined execution
= Number of instructions executed per unit time
= 1000 tasks / 100300 ns

## Slide 13
Problem-02:
A four-stage pipeline has the stage delays as 150, 120, 160 and 140 ns respectively. Registers are used between the stages and have a delay of 5 ns each. Assuming constant clocking rate, the total time taken to process 1000 data items on the pipeline will be-
120.4 microseconds
160.5 microseconds
165.5 microseconds
590.0 microseconds

## Slide 14
Solution-
Given-
Four stage pipeline is used
Delay of stages = 150, 120, 160 and 140 ns
Delay due to each register = 5 ns
1000 data items or instructions are processed
Cycle Time-
Cycle time
= Maximum delay due to any stage + Delay due to its register
= Max {150, 120, 160, 140} + 5 ns
= 160 ns + 5 ns
= 165 ns

## Slide 15
Pipeline Time to Process 1000 Data Items-
Pipeline time to process 1000 data items
= Time taken for 1st data item + Time taken for remaining 999 data items
= 1 x 4 clock cycles + 999 x 1 clock cycle
= 4 x cycle time + 999 x cycle time
= 4 x 165 ns + 999 x 165 ns
= 660 ns + 164835 ns
= 165495 ns
= 165.5 μs
Thus, Option (C) is correct.

## Slide 16
References
Reference Books:
J.P. Hayes, “Computer Architecture and Organization”, Third Edition.
Mano, M., “Computer System Architecture”, Third Edition, Prentice Hall.
Stallings, W., “Computer Organization and Architecture”, Eighth Edition, Pearson Education.
Text Books:
Carpinelli J.D,” Computer systems organization &Architecture”, Fourth Edition, Addison Wesley.
Patterson and Hennessy, “Computer Architecture”, Fifth Edition Morgaon Kauffman.

## Slide 17
Other References:
https://www.gatevidyalay.com/instruction-pipelining-performance/
https://www.studytonight.com/computer-architecture/pipelining
https://www.gatevidyalay.com/pipelining-practice-problems/
Video Links:
https://youtu.be/DpMVYR8FauE?si=9S9uKDCVeDSDBwLX
https://youtu.be/HhAnkFR-IWE?si=lSOPXH-SLDVx6yrA
https://www.youtube.com/live/rQl8WxeUdf0?si=dVdXkTphehYcnkRh